## Slide 1: Advanced Computer Architecture (ACA 2018)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2018

## Slide 2: Quiz 1 - Functions of X Y Z … 2min

## Slide 3: Lecture 02 ISA
October 16, 2018

## Slide 4: Objects Today
Storage
  Memory
  Regesters
Operands
Operations
Format of instructions
Addressing

## Slide 5: What Is a Memory?
A container of binary number
How to specify a memory?
  How many binary cells (bits) can be accessed in one time? -- the object size
    8 bits in our book and most computer
    8 bits == a byte
  How many bytes in all? -- the memory size
  Where is the cell position? -- the address

## Slide 6: Accessing Mode
Bytes (8 bits)
Half words (16 bits)
Words (32 bits)
Double words (64 bits)
How to access these units?
  Programming in your code
  Test
  suggestion: in procedures

## Slide 7: The Little and Big Endian
bit | 0 | 7 | 8 | 15 | 16 | 23 | 24 | 31
 | byte #0 |  | byte #1 |  | byte #2 |  | byte #3 | 
 | 16-bit integer #0 |  |  |  | 16-bit integer #1 |  |  | 
 | 32-bit integer |  |  |  |  |  |  | 
0x | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
big-endian | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000
 | Most-S |  |  |  | Least-S |  |  | 
little-endian | Least-S |  |  |  | Most-S |  |  | 
 | 0111 | 1000 | 0101 | 0110 | 0011 | 0100 | 0001 | 0010

## Slide 8: Byte Aligned
An access to an object of size s bytes at byte address A is aligned if
A mod s = 0
  Figure A.5/page A8
Width of object | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Byte |  |  |  |  |  |  |  | 
Half word |  |  |  |  |  |  |  | 
Word |  |  |  |  |  |  |  | 
Double word |  |  |  |  |  |  |  | 

## Slide 9: Registers
Another forms of storage internal to the CPU

## Slide 10: Three Types of Register File
Accumulator architecture
Stack architecture
Register Architecture

## Slide 11: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Format of instructions
Addressing

## Slide 12: Type and Size of Common Operands
Character | (1 byte)
Integer | Half word (16-bit short integer) Word (32-bit integer) Long word (64-bit integer)
Floating point (Real) | Word (32-bit single-precision number) Double word (64-bit double-precision number)
Decimal | Unpacked decimal A decimal characters string Packed decimal 4-bit to encode values 0-9, usually based on BCD code A two decimal digits packed into each byte

## Slide 13: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Addressing
Format of instructions

## Slide 14: Operations: Types of Instructions
Operations | Examples
Arithmetic & logical | Integer: ADD, AND, OR, etc.
Data transfer | LOADS and STORES
Control | JUMP, CALL, RETURN TRAPS, etc.
System | OS call, virtual memory instructions
Floating point | Floating point: ADD, AND, OR, etc.
Decimal | Decimal: ADD, AND, conversion, etc.
String | String: MOVE, COMP, SEARCH, etc.
Graphics | Pixel operations, compression, etc.

## Slide 15: The Top 10 Instructions for the 80x86 (SPECint92)
Rank | 80x86 instruction | Integer average( % total executed)
1 | load | 22%
2 | conditional branch | 20%
3 | compare | 16%
4 | store | 12%
5 | add | 8%
6 | and | 6%
7 | sub | 5%
8 | move register-register | 4%
9 | call | 1%
10 | return | 1%
total |  | 96%

## Slide 16: Branch Instructions
Conditional branch -- branch
Unconditional branch -- jump
Call
Return

## Slide 17: The Frequencies of Control Flow Instructions

## Slide 18: Methods to Evaluation Branch Conditions
Name | How condition is tested
Condition code (CC) | Special bits are set by ALU operations
Condition register | Set arbitrary register with the result of a comparison
Compare and branch | Branch is part of the compare

## Slide 19: Branch Distances
Branch distances in terms of number of instructions between the target and the branch instruction

## Slide 20: Frequency of Types of Compares in Conditional Branches

## Slide 21: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Format of instructions
Addressing

## Slide 22: The Pop Addressing Modes
Addressing mode | Example instruction | Usage
Register | ADD R3,R4 | Value is in register
Immediate | ADD R4,#3 | Constants
Displacement | ADD R4,100(R1) | Local variables
Register indirect | ADD R4,(R1) | Pointers
Indexed | ADD R3,(R1+R2) | Array
Direct or absolute | ADD R1,(1001) | Static data
Mem. Indirect | ADD R1,@(R3) | Pointers
Auto increment | ADD R1,(R2)+ | Stepping
Auto decrement | ADD R1,-(R2) | As inc.
Scaled | ADD R1,100(R2)(R3) | To index array

## Slide 23: Immediate Operand
About one-quarter of data transfers and ALU operations have an immediate operand

## Slide 24: Immediate Values
16 bits would capture about 80% and 8 bits about 50% of immediates
  about 20% to 25% were longer than 16 bits

## Slide 25: Use of Memory Addressing Modes
Almost all the memory indirect references use displacement mode as the base
Displacement mode includes all displacement lengths (8, 16, and 32 bits)

## Slide 26: Displacement Values Distributions
These data were taken on the Alpha architecture with full optimization for SPEC CPU2000, showing the average of integer programs (CINT2000) and the average of floating-point programs (CFP2000)

## Slide 27: Structure of a Copmuter
Storage
  Memory
  Regesters
Operands
Operations
Format of instructions
Addressing

## Slide 28: How to Encoding an Instruction Set
What fields must a instruction has?
How big the operations fields?
How many address fields must it has?
How long a address field ought to be?
Something else?

## Slide 29: Three Basic Variations in Instruction Encoding

## Slide 30: Reduced Code Size in RISCs
Several manufacturers offered a new hybrid version of their RISC instruction sets
  With both 16-bit and 32-bit instructions, even 64-bit
  The narrow instructions support
    Fewer operations
    Smaller address and immediate fields
    Fewer registers
    Two-address format

## Slide 31: Reduced Code Size in RISCs
The ARM Thumb and MIPS MIPS16, which both claim a code size reduction of up to 40%
  Instruction caches act as if they are about 25% larger
IBM’s CodePack: compresses its standard instruction set
  An overall performance cost of 10%, resulting in a code size reduction of 35% to 40%
Hitachi invented a fixed 16-bit RISC instruction set, called SuperH

## Slide 32: A "Typical" RISC ISA
32-bit fixed format instruction
32 32-bit GPR (R0 == 0, DP takes pair)
3-address, reg-reg arithmetic instruction
Single address mode for load/store
Simple branch conditions
Delayed branch
SPARC, MIPS, HP PA, DEC Alpha, IBM PowerPC, CDC6600, CDC7600, Cray-1, Cray-2...

## Slide 33: Instruction Format
These four formats are found in all five architectures
  Op = the main opcode
  Opx = an opcode extension
  Rd = the destination register
  Rs1 = source register 1
  Rs2 = source register 2
  Const = a constant
    used as an immediate, address, mask, or sift amount

## Slide 34: Distribution of Data Accesses by Size

## Slide 35: The Structure of Compilers

## Slide 36: Major Types of Optimizations and Examples

## Slide 37: Change In Instruction Count as Compiler Optimization Levels

## Slide 38: The Lineage of RISC Instruction Sets

## Slide 39: Berkeley New ISA, RISC-V
RISC-V is a new simple, clean, extensible ISA we developed at Berkeley for education and research
  RISC-I/II, Berkeley RISC implementations
  Berkeley research machines SOAR/SPUR considered RISC-III/IV
Both of the dominant ISAs (x86 and ARM) are too complex to use for teaching
RISC-V ISA manual available on web page
Full GCC-based tool chain available
Version 1.0 published on March 28, 2012
  Based on experience with all these previous projects, the RISC-V ISA definition was begun in summer 2010

## Slide 40: The RISC-V Instruction Set Manual
RISC-V is a new ISA designed to support computer architecture research and education
Our goals in defining RISC-V include:
  Provide a realistic but open ISA that captures important details of commercial general-purpose ISA designs and that is suitable for direct hardware implementation.
  Provide a small but complete base ISA that avoids “over-architecting” for a particular microarchitecture style (e.g., microcoded, in-order, decoupled, out-of-order) or implementation technology (e.g., full-custom, ASIC, FPGA), but which allows efficient implementation in any of these
  Support both 32-bit and 64-bit address space variants for applications, operating system kernels, and hardware implementations.
  Support highly-parallel multicore or manycore implementations, including heterogeneous multiprocessors.
  Support an efficient dense instruction encoding with variable-length instructions, improving performance and reducing energy and code size.
  Support the revised 2008 IEEE 754 floating-point standard.
  Be fully virtualizable.
  Be simple to subset for educational purposes and to reduce complexity of bringing up new implementations.
  Support experimentation with user-level ISA extensions and specialized variants.
  Support independent experimentation with new supervisor-level ISA designs

## Slide 41: RISC-V ISA
New fifth-generation RISC design from UC Berkeley
Realistic & complete ISA, but open & small
Not over-architected for a certain implementation style
Both 32-bit (RV32) and 64-bit (RV64) address-space variants
Designed for multiprocessing
Efficient instruction encoding
Easy to subset/extend for education/research
Techreport with RISC-V spec available on class website
Increasing momentum with industry adoption
Please see CS61C Fall 2017, Lectures 5-7 for RISC-V ISA review:
http://inst.eecs.berkeley.edu/~cs61c/fa17/

## Slide 42: RISC-V Has Three Base Instructions Sets

## Slide 43: RV32 Processor State
Program counter (pc)
32x32-bit integer registers (x0-x31)
x0 always contains a 0
32 floating-point (FP) registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fsr), used for FP rounding mode & exception reporting

## Slide 44: RISC-V Instruction Length Encoding
All the 32-bit instructions in the base ISA have their lowest two bits set to 11
The compressed 16-bit instruction-set extensions have their lowest two bits equal to 00, 01, or 10
Instruction-set extensions encoded with more than 32 bits have additional low-order bits set to 1

## Slide 45: RISC-V Dynamic Instruction Mix for the SPECint2006 Programs

## Slide 46: Reading – 10min Presentations
Textbook
  Appendix A
    A.1~A.9: more attention in A.9
      A.9 Putting It All Together: The RISC-V Architecture
Papers
  "The Case for the Reduced Instruction Set Computer", Patterson, Ditzel, 1980
  Comments on the "The Case for the RISC", Clark, Strecker, 1980
Homeworks

## Slide 47: Coding – in 2 Weeks
RISC V Specification v2.1
  Report in next lecture
All instructions in RISC V 2.1 RV32I&RV32E subset
Only the function without the time charactor of the instruction is specified by the program
Test the functions
Exchange your code and then integrate all code
These two weeks
Homeworks

## Slide 48: Next…
A Processor