## Slide 1: Advanced Computer Architecture (ACA 2018)
Prof. SHEN Li
College of Computer, NUDT
Fall, 2018

## Slide 2: Lecture 03 Pipeline
October 24, 2018

## Slide 3: Objects Today
The Basic 5-Stage Pipeline
Pipeline Hazard
  Methods to Avoid Hazard
The Implementation of Pipelines
Exceptions and Interrupts

## Slide 4: 5 Steps of MIPS Datapath
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
L
M
D
ALU
MUX
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
4
Adder
Zero?
Next SEQ PC
Address
Next PC
WB Data
Inst
RD
RS1
RS2
Imm
IR <= mem[PC];
PC <= PC + 4
Reg[IRrd] <= Reg[IRrs] opIRop Reg[IRrt]

## Slide 5: Inst. Set Processor Controller
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
r <= A opIRop B
Reg[IRrd] <= WB
WB <= r
Ifetch
opFetch-DCD
PC <= IRjaddr
if bop(A,b)
PC <= PC+IRim
br
J
RR
r <= A opIRop IRim
Reg[IRrd] <= WB
WB <= r
RI
r <= A + IRim
WB <= Mem[r]
Reg[IRrd] <= WB
LD
ST
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
Ifetch
opFetch-DCD
PC <= IRjaddr
if bop(A,b)
PC <= PC+IRim
br
J
JR
JAL

## Slide 6: Pipelined MIPS
The appropriate registers between each pipeline stage are called
  Pipeline registers or pipeline latches
The registers are labeled with the names of the stages they connect
  IF/ID -- ID/EX -- EX/MEM -- MEM/WB

## Slide 7: Pipelined Datapath: Original
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Ext
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we

## Slide 8: Pipelined Datapath: With latches and Stages
write
-back
phase
fetch
phase
execute
phase
decode & Reg-fetch
phase
memory
phase
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Ext
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
IR
PC

## Slide 9: Pipelined Datapath: Clock Cycle Time
Clock cycle time can be reduced by dividing the execution of an instruction into multiple cycles
tC > max {tIM, tRF, tALU, tDM, tRW} (= tDM probably)
write
-back
phase
fetch
phase
execute
phase
decode & Reg-fetch
phase
memory
phase
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Ext
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
IR
PC

## Slide 10: Visualizing and Ideal Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 11: Next …
Appendix C2:
Pipelining Hurdle - Hazards

## Slide 12: Limitation to pipelining: Hazards
HAZARDS prevent next instruction from executing during its designated clock cycle
Three classes of hazards
  STRUCTURAL hazards: HW cannot support this combination of instructions
  DATA hazards: Instruction depends on result of prior instruction still in the pipeline
  CONTROL hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow

## Slide 13: Structure Hazards: One Port Memory
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 14: Structure Hazards: Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 15: Data Hazards on R1
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 16: Types of Data Hazards
When an instruction depends on the RESULTS of a previous instruction in a way that is exposed by the overlapping of instructions in the pipeline
  Read after write
  Write after read
  Write after write
  Read after read (?)

## Slide 17: Data Hazards of “r1”
Read After Write (RAW)
  I: add r1,r2,r3
  J: sub r4,r1,r3
Write After Read (WAR)
  I: sub r4,r1,r3
  J: add r1,r2,r3
Write After Write (WAW)
  I: sub r1,r4,r3
  J: add r1,r2,r3

## Slide 18: Forwarding to avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 19: Hardware Changes for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux

## Slide 20: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 21: Data Hazard Even with Forwarding
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg

## Slide 22: Control Hazard on Branches
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11

## Slide 23: The Revised Pipeline
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 24: Control Hazard on Branches
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11

## Slide 25: Four Branch Hazard Alternatives
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
#3: Predict Branch Taken
#4: Delayed Branch

## Slide 26: Next…
Appendix C2: Branch Penalties Reducing

## Slide 27: Dealing the branch delay in compiler
The actions for a branch are static
  Static — they are fixed for each branch during the entire execution
The software can try to minimize the branch penalty using knowledge
  of the hardware scheme
  of branch behavior
Chapters 3 looks at more powerful hardware and software techniques for both static and dynamic branch prediction

## Slide 28: Four Simple Compilation Strategies
Freeze
  Flush the pipeline
Predicted-not-taken
  Predicted-untaken scheme
Treat every branch as taken
Delayed branch
  This technique was heavily used in early RISC processors and works reasonably well in the five-stage pipeline

## Slide 29: Untaken and Taken in a Predicted-not-taken
Untaken
Taken
Branch target
When the branch is untaken, determined during ID, we have fetched the fall-through and just continue
If the branch is taken during ID, we restart the fetch at the branch target
  This causes all instructions following the branch to stall 1 cycle

## Slide 30: Delayed Branch
In a delayed branch, the execution cycle with a branch delay of one is
  branch instruction
  sequential successor1
  branch target if taken
The sequential successor is in the branch delay slot
This instruction is executed whether or not the branch is taken

## Slide 31: The Behavior of A Delayed Branch
The instructions in the delay slot are executed
  If the branch is untaken, execution continues with the instruction after the branch delay instruction
  If the branch is taken, execution continues at the branch target
Branch delay instruction ( i+1 )
Branch delay instruction ( i+1 )
untaken
taken

## Slide 32: Scheduling the Branch Delay Slot
the best choice
reached by another path
R7 were an unused register

## Slide 33: Delayed Branch Slot(s) Processing
Almost all processors with delayed branch have a single instruction delay
  It is possible to have a branch delay longer than one
When the instruction in the branch delay slot is also a branch, the meaning is unclear
  If the branch is not taken, what should happen to the branch in the branch delay slot?
  Because of this confusion, architectures with delay branches often disallow putting a branch in the delay slot

## Slide 34: Next …
Static Branch Prediction

## Slide 35: The Simplest Scheme: Predict as Taken
An average misprediction rate that is equal to the untaken branch frequency
For the SPEC programs is 34%
Unfortunately, the misprediction rate for the SPEC ranges from not very accurate (59%) to highly accurate (9%)

## Slide 36: Direction-based Prediction
A Better Alternative
Predict on the basis of branch direction
  Backward-going branches to be TAKEN
  Forward-going branches to be NOT TAKEN
In the SPEC, More than half of the forward-going branches are taken
  -> predicting branches as taken is better
For other benchmarks or compilers, misprediction rate is 30% to 40%

## Slide 37: An Enhanced Direction-based Prediction
Uses program context information
  Using previous branch information
Generates more accurate predictions than a simple scheme based solely on branch direction

## Slide 38: Profile-based Prediction
A More Accurate Technique
Predict branches on the basis of profile information collected from earlier runs
  An individual branch is often highly biased toward taken or untaken
  Changing the input leads to only a small change in the prediction accuracy

## Slide 39: Profile-based Prediction: Misprediction
Varies widely
  The FP, an average rate of 9% with a standard deviation of 4%
  The integer, an average rate of 15% with a standard deviation of 5%

## Slide 40: Instructions between Misprediction
Varies widely
  The FP, an average rate of 9% with a standard deviation of 4%
  The integer, an average rate of 15% with a standard deviation of 5%

## Slide 41: Usage of Static Branch Prediction
Static
  Sometimes be used in processors where the expectation is that branch behavior is highly predictable at compile-time
  Also be used to assist dynamic predictors
Compiler

## Slide 42: Next …
The Simplest Dynamic Branch Prediction – Branch-Prediction Buffer (BPB)

## Slide 43: A General Dynamic Branch Prediction Scheme
Incoming stream of addresses
Fast outgoing stream of predictions
Correction information returned from pipeline
Branch
Predictor
Incoming Branches
{ Address }
Prediction
{ Address, Value }
Corrections
{ Address, Value }
History
Information

## Slide 44: BPB Principles
The simplest dynamic branch prediction
  Check the branch taken/untaken last time
A BPB is a small memory
  1 bit says whether branch taken last time
  Indexed by the lower bits of the branch instruction address
  If the prediction turns out to be wrong, the bit is inverted
  It is also called Branch History Buffer (BHB)
 | Predictor 0
 | Predictor 1
lower | 
bits | 
of the | 
branch | 
PC | 
 | Predictor 2n-1

## Slide 45: 1-bit BPB Scheme
Prediction accuracy is about 80%
  Almost all loop will predict incorrectly twice

## Slide 46: 2-bit BPB Scheme
A prediction must miss twice in a row before the prediction is changed
Studies using SPEC89 have shown
  A hit rate 82~99% for a 4K entries buffer
  The highest accuracy comes in which have lots of loops
  Straight-line code has the worst accuracy

## Slide 47: States in a 2-bit Scheme
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 48: BPB Examples
Consider a loop
  Branch behavior is taken 9 times in a row
  Then not taken once
What is the prediction accuracy for this branch?
  Original states: not taken(0)

## Slide 49: BPB Examples - Answer
Mispredict twice: the first and last loop iterations.
  The first iteration: the loop taken
  The last iteration: the loop not taken
loop 1 (0-1/1) > loop 2 (1-1/1) …… > loop 9 (1-1/1) > loop 10 (1-0/0)
Two important concepts
  The prediction accuracy: 80%
  The branch taken rate: 90%

## Slide 50: BPB Examples - Accuracy
Prediction accuracy of a 4K-entry 2-bits BPB for SPEC89 (IBM Power)
  Accuracy: 82% ~ 99%
  Integer benchmarks: average mis 11%
    gcc, espresso, eqntott, li
  FP benchmark: average mis 4%
    nasa7, matrix300, tomcatv
  Why they are deference?

## Slide 51: Mispredictions

## Slide 52: States in a 2-bit Scheme: an Alternation
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 53: n-bit branch predictor
The predictor counter can take on values between 0~(2n–1)
  Counter≥2n–2, predicted as taken
  Otherwise, predicted untaken
Studies shown: the n-bit predictors and the 2-bit predictors do almost as well
  Most systems rely on 2-bit branch predictors rather than n-bit predictors
Question
  How many entries of a BPB is batter?

## Slide 54: Entries’ Mis : 4K vs. Unlimited, 2bit/entry

## Slide 55: BPB: Typical Implementation
As a small, special-purpose “cache”
  which is accessed with the instruction address during the IF pipe stage
As bits that are attached to instruction cache and fetched with each instruction
  If the instruction is decoded as a branch -> the bits fetched predict it as
    Taken -> fetching begins from the target as soon as the PC is known
    Not taken -> sequential fetching continues

## Slide 56: BPB: illustrations
Lower bits of branch address | … |  |  | Lower bits of branch address | … | …
1-bit scheme |  |  | 2-bit scheme |  |  | 

## Slide 57: BPB: Instruction Fetch
0
0
Fetch PC

## Slide 58: BPB: Accessing I-Cache and BPB
0
0
Fetch PC
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 59: BPB: Instruction Decoding and Correctness Checking
2K-entry BPB, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 60: Next ...
Appendix C4
What makes Piplining Hard to Implement ?

## Slide 61: Exception and Interrupt
Exception
  An unusual event happens to an instruction during its execution
  Examples: divide by zero, undefined opcode
Interrupt
  Hardware signal to switch the processor to a new instruction stream
  Example: a key pressed

## Slide 62: Exception and Interrupt Types
I/O device request
Invoking an operating system service from a user program
Tracing instruction execution or breakpoint (programmer-requested interrupt)
Page fault (not in main memory)
Memory-protection violation

## Slide 63: Problems
It must appear that the exception or interrupt must appear between 2 instructions (Ii and Ii+1)
  The effect of all instructions up to and including Ii is totally complete
  No effect of any instruction after Ii can take place
The interrupt (exception) handler either aborts program or restarts at instruction Ii+1

## Slide 64: Safety Steps
Force a trap instruction into the pipeline on the next IF
Until the trap is taken, turn off all writes for the faulting instruction
The following exception-handling routine immediately saves the PC of the faulting instruction

## Slide 65: Precise Exceptions
If the pipeline can be stopped just before the faulting instruction are completed and those after it can be restarted from scratch
Any processor with demand paging or IEEE arithmetic trap handlers must make its exceptions precise

## Slide 66: Precise Exceptions in Static Pipelines
Key observation: architected state only change in memory and register write stages

## Slide 67: Next ...
Appendix C5
Multicycle Operations

## Slide 68: Handle Multicycle Operations
The floating-point pipeline will allow for a longer latency for operations
The EX cycle may be repeated as many times as needed to complete the operation
The number of repetitions can vary for different operations
There may be multiple FP functional units
  A structural hazard for the FU it uses
  Or cause a data hazard

## Slide 69: Four Separate FUs In Our MIPS

## Slide 70: Latency and Initiation Interval
Functional unit | Latency | Initiation interval
Integer ALU | 0 | 1
Data memory (int & FP loads) | 1 | 1
FP add | 3 | 1
FP multiply (also int. multiply) | 6 | 1
FP divide (also integer divide) | 24 | 25

## Slide 71: The Pipelines

## Slide 72: How Big a Chip

## Slide 73: How Big a Chip

## Slide 74: Berkeley RISC Chips
RISC-I (1982)
  Contains 44,420 transistors
  Fabbed in 5 µm NMOS, ran at 1 MHz with a die area of 77 mm2
  This chip is probably the first VLSI
RISC RISC-II (1983)
  Contains 40,760 transistors
  Fabbed in 3 µm NMOS, ran at 3 MHz, and the die size is 60 mm2
74

## Slide 76: Big PIC of RISC II
RISC-I (1982)
  Contains 44,420 transistors
  Fabbed in 5 µm NMOS, ran at 1 MHz with a die area of 77 mm2
  This chip is probably the first VLSI
RISC RISC-II (1983)
  Contains 40,760 transistors
  Fabbed in 3 µm NMOS, ran at 3 MHz, and the die size is 60 mm2

## Slide 77: John L. Hennessy
Over the years, the duties of a university president have expanded dramatically. Stanford's president remains focused on and rooted in academics, but the job entails much more. Raising money, making decisions about future land use and addressing the needs of a medical center are just a few of the responsibilities of Stanford's tenth president, John L. Hennessy.
Stanford MIPS processor

## Slide 78: Reading Paper

## Slide 79: Reading – 10min Presentations
Textbook
  Appendix C
Papers
  ”Design and Implementation of RISC I", C.H. Sequin and D.A. Patterson, Proc. Advanced Course on VLSI architecture, 1982
Homeworks

## Slide 80: Next…
Appendix C7: A Dynamic Scheduled
Pipeline – Scoringboard