## Slide 1: Advanced Computer Architecture (ACA 2018)
Prof. SHEN Li
College of Computer, NUDT
Fall, 2018

## Slide 2: Lecture 05 ILP & Loop Unrolling
November 07, 2018

## Slide 3: How Changes Bursted: Reformation to Revolution
IBM PC
  Personal Computing
  Ad, 11/81
  Giant

## Slide 5: IBM PC, 1981
Hardware
  Team from IBM building PC prototypes in 1979
  Motorola 68000 chosen initially, but 8086 was late
  IBM builds “stopgap” prototypes using 8088 boards from Display Writer word processor
  8088 is 8-bit bus version of 8086 => allows cheaper system
  Estimated sales of 250,000 => 100,000,000s were sold
Software
  Microsoft negotiates to provide OS for IBM
    Later buys and modifies QDOS from Seattle Computer Products
Open System
  Standard processor, Intel 8088
  Standard (hardware) system interfaces => 8088 extension => ISA standard buses
  Standard OS, MS-DOS, PC-DOS, DR-DOS ...
  IBM permits cloning and third-party software

## Slide 6: Exploiting ILP Goal: Minimize CPI
Pipeline CPI = Ideal pipeline CPI
+ Structural stalls
+ Data hazard stalls
+ Control stalls
The ideal pipeline CPI is a measure of the maximum performance attainable by the implementation

## Slide 7: The Major ILP Techniques 1/2
Technique | Reduces | Section
Forwarding and bypassing | Potential data hazard stalls | C.2
Delayed branches and simple branch scheduling | Control hazard stalls | C.2
Basic compiler pipeline scheduling | Data hazard stalls | C.2, 3.2
Basic dynamic scheduling (scoreboarding) | Data hazard stalls from true dependences | C.7
Loop unrolling | Control hazard stalls | 3.2
Branch prediction | Control stalls | 3.3

## Slide 8: The Major ILP Techniques 2/2
Technique | Reduces | Section
Dynamic scheduling with renaming | stalls from Data hazard, output dependences and antidependences | 3.4
Hardware speculation | Data hazard and control hazard stalls | 3.6
Dynamic memory disambiguation | Data hazard stalls with memory | 3.6
Issuing multiple instructions per cycle | Ideal CPI | 3.7, 3.8
Compiler dependence analysis, software pipelining, trace scheduling | Ideal CPI, data hazard stalls | H.2, H.3
Hardware support for compiler speculation | Ideal CPI, data hazard stalls, branch hazard stalls | H.4, H.5

## Slide 9: Techniques and Reduces: Hardware
Techniques | Reduces
Forwarding and bypassing | Potential data hazard stalls
Delayed branches and simple branch scheduling | Control hazard stalls
Basic dynamic scheduling (scoreboarding) | Data hazard stalls from true dependences
Dynamic scheduling with renaming | Data hazard stalls and stalls from anti- and output dependences
Dynamic branch prediction | Control stalls
Issuing multiple instructions per cycle | Ideal CPI
Hardware Speculation | Data hazard and control hazard stalls
Dynamic memory disambiguation | Data hazard stalls with memory

## Slide 10: Dependences, Hazard and Stall
Dependences are a property of programs
But
  A dependence results in an actual hazard?
  That hazard actually causes a stall?
The presence of the dependence indicates the potential for a hazard
  This is critical to understanding how ILP is exploited

## Slide 11: Data Hazards
A hazard is created by dependence between instructions
  They are close enough
  The overlap during execution
  > Change the order of access to the operand involved in the dependence
Three types of data hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)

## Slide 12: Data Hazards: An Example
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 13: Data Hazards: RAW Hazard - 1
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 14: Data Hazards: RAW Hazard - 1
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 15: Data Hazards: RAW Hazard - 3
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 16: Data Hazards: RAW Hazard - 4
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 17: Data Hazards: WAR Hazard - 1
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 18: Data Hazards: WAR Hazard - 2
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 19: Data Hazards: WAW Hazard - 1
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2

## Slide 20: Data Hazards: All
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
I6
I2
I4
I1
I5
I3
Execuation order
  In-order
  Out-of-order (o-o-o)

## Slide 21: Instruction Scheduling: Valid Order
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
I6
I2
I4
I1
I5
I3
in-order | I1 | I2 | I3 | I4 | I5 | I6
o-o-o |  |  |  |  |  | 
o-o-o |  |  |  |  |  | 

## Slide 22: Instruction Scheduling: Out of Order
in-order | I1 | I2 | I3 | I4 | I5 | I6
o-o-o | I2 | I1 | I3 | I4 | I5 | I6
o-o-o | I1 | I2 | I3 | I5 | I4 | I6
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
I6
I2
I4
I1
I5
I3

## Slide 23: Latency of Instructions: Assumption
Latency*
I1 DIVD f6, f6, f4 4
I2 LD f2, 45(r3) 1
I3 MULTD f0, f2, f4 3
I4 DIVD f8, f6, f2 4
I5 SUBD f10, f0, f6 1
I6 ADDD f6, f8, f2 1
*The latencies are extra cycles to the 5-stage

## Slide 24: In-order Issue and In-order Completion
I1 DIVD f6, f6, f4 4
I2 LD f2, 45(r3) 1
I3 MULTD f0, f2, f4 3
I4 DIVD f8, f6, f2 4
I5 SUBD f10, f0, f6 1
I6 ADDD f6, f8, f2 1
clk | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
in/in | 1 | 2 |  |  | 1 | 2 | 3 | 4 |  | 3 | 5 | 4 | 6 | 5 | 6

## Slide 25: In-order Issue and Out-of-order Completion
I1 DIVD f6, f6, f4 4
I2 LD f2, 45(r3) 1
I3 MULTD f0, f2, f4 3
I4 DIVD f8, f6, f2 4
I5 SUBD f10, f0, f6 1
I6 ADDD f6, f8, f2 1
clk | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
in/in | 1 | 2 | 2 | 3 | 1 | 4 | 3 | 5 | 5 | 4 | 6 | 6 |  |  | 

## Slide 26: Usage:
Loop Unrolling
& Instruction Scheduling

## Slide 27: Assumptions
The standard 5-stage integer pipeline
FUs are fully pipelined or replicated
Branches have a delay of 1 clock cycle
Previous conditions instruction have a delay of 1 clock cycle just before branch
An integer load latency of 1
An integer ALU operation latency of 0

## Slide 28: The Revised Pipeline
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 29: Control Hazard and Branches
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 30: Latency of FP Operations
Instruction producing result | Instruction using result | Latency in cycles
FP ALU op | Another FP ALU op | 3
FP ALU op | Store double | 2
Load double | FP ALU op | 1
Load double | Store double | 0

## Slide 31: Code Example - C
for (i=999; i>=0; i=i–1)
x[i] = x[i] + s;

## Slide 32: Code Example - MIPS
Loop: L.D F0,0(R1) ;F0=vector element
ADD.D F4,F0,F2 ;add scalar from F2
S.D 0(R1),F4 ;store result
DADDUI R1,R1,#-8 ;dec pointer 8B (DW)
BNE R1,R2,Loop ;branch R1!=R2
R1: initially highest address of the array
R2: pre-computed to last element address - 8

## Slide 33: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)

## Slide 34: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | ? ADD.D F4,F0,F2
Load double used by a FP ALU op, the Latency in 1 cycle

## Slide 35: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2

## Slide 36: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | ? S.D 0(R1),F4
a FP ALU op used by a Store double , the Latency in 2 cycle

## Slide 37: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | ? S.D 0(R1),F4
a FP ALU op used by a Store double , the Latency in 2 cycle
This is the second

## Slide 38: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
a FP ALU op used by a Store double , the Latency in 2 cycle
there are two stall cycles

## Slide 39: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | ?DADDUI R1,R1,#-8

## Slide 40: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8

## Slide 41: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8
8 | ? BNE R1,R2,Loop

## Slide 42: The Loop Execution without Scheduling
what is the next?
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8
8 | Stall
9 | BNE R1,R2,Loop

## Slide 43: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8
8 | Stall
9 | BNE R1,R2,Loop
10 | ?

## Slide 44: The Loop Execution without Scheduling
Clock | Unscheduled
1 | L.D F0,0(R1)
2 | Stall
3 | ADD.D F4,F0,F2
4 | Stall
5 | Stall
6 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8
8 | Stall
9 | BNE R1,R2,Loop
10 | Stall

## Slide 45: The Loop Execution without Scheduling
10 clock cycles an iteration
Just 3 for execution (L.D, ADD.D, S.D)
  30%
  5 clock cycles of stall (50%)
  2 for loop overhead (20%)
Rewrite code to minimize stalls?

## Slide 46: Scheduling: Rewrite the Code!
Clk | Unscheduled | Scheduled
1 | L.D F0,0(R1) | L.D F0,0(R1)
2 | Stall | 
3 | ADD.D F4,F0,F2 | 
4 | Stall | 
5 | Stall | 
6 | S.D 0(R1),F4 | 
7 | DADDUI R1,R1,#-8 | 
8 | Stall | 
9 | BNE R1,R2,Loop | 
10 | Stall | 

## Slide 47: Scheduling the loop
Clk | Unscheduled | Scheduled
1 | L.D F0,0(R1) | L.D F0,0(R1)
2 | Stall | DADDUI R1,R1,#-8
3 | ADD.D F4,F0,F2 | 
4 | Stall | 
5 | Stall | 
6 | S.D 0(R1),F4 | 
7 | DADDUI R1,R1,#-8 | 
8 | Stall | 
9 | BNE R1,R2,Loop | 
10 | Stall | 

## Slide 48: Scheduling the loop
Clk | Unscheduled | Scheduled
1 | L.D F0,0(R1) | L.D F0,0(R1)
2 | Stall | DADDUI R1,R1,#-8
3 | ADD.D F4,F0,F2 | ADD.D F4,F0,F2
4 | Stall | ??
5 | Stall | ??
6 | S.D 0(R1),F4 | S.D 8(R1),F4
7 | DADDUI R1,R1,#-8 | 
8 | Stall | 
9 | BNE R1,R2,Loop | 
10 | Stall | 

## Slide 49: Scheduling the loop
Clk | Unscheduled | Scheduled
1 | L.D F0,0(R1) | L.D F0,0(R1)
2 | Stall | DADDUI R1,R1,#-8
3 | ADD.D F4,F0,F2 | ADD.D F4,F0,F2
4 | Stall | Stall
5 | Stall | BNE R1,R2,Loop
6 | S.D 0(R1),F4 | S.D 0(R1),F4
7 | DADDUI R1,R1,#-8 | 
8 | Stall | 
9 | BNE R1,R2,Loop | 
10 | Stall | 

## Slide 50: The Loop with and without Scheduling
6 clock cycles an iteration
The speedup is 10/6=1.7
Still just 3 for execution (L.D, ADD.D, S.D)
  50%
  1 clock cycle of stall (17%)
  2 clock cycles for loop overhead (33%)
How to minimize stalls and get rid of the overhead cycles?

## Slide 51: Loop Unrolling

## Slide 52: Codes – Unrolled the Loop
Assuming the vector contains some multiple of 4 elements
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4 ;drop DADDUI & BNE
L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4 ;drop DADDUI & BNE
L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4 ;drop DADDUI & BNE
L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4
DADDUI R1,R1,#-32
BNE R1,R2,Loop

## Slide 53: Codes – Execution Time
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4
L.D F0,-8(R1)
ADD.D F4,F0,F2
S.D -8(R1),F4
L.D F0,-16(R1)
ADD.D F4,F0,F2
S.D -16(R1),F4
L.D F0,-24(R1)
ADD.D F4,F0,F2
S.D -24(R1),F4
DADDUI R1,R1,#-32
BNE R1,R2,Loop
stall
start waiting, …, execute
1
2,3
4,5,6
7
8,9
10,11,12
13
14,15
16,17,18
19
20,21
22,23,24
25
26,27
28

## Slide 54: Codes – Cost Analysis
This loop will run in 28 clock cycles
  14 stalls
    Each L.D has 1 stall - 4
    Each ADD.D 2 stall - 8
    The DADDUI 1 stall - 1
    The branch 1 stall - 1
  Plus 14 instruction issue cycles
7 clock cycles per iteration
8 Registers

## Slide 55: Codes – Register Renaming
If we simply replicated the instructions when we unrolled the loop, the resulting use of the same registers could prevent us from effectively scheduling the loop
Use different registers for each iteration
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D 0(R1),F4
L.D F6,-8(R1)
ADD.D F8,F6,F2
S.D -8(R1), F8
L.D F10,-16(R1)
ADD.D F12,F10,F2
S.D -16(R1), F12
L.D F14,-24(R1)
ADD.D F16,F14,F2
S.D -24(R1), F16
DADDUI R1,R1,#-32
BNE R1,R2,Loop

## Slide 56: Codes – Scheduling to eliminate all stalls
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1)
L.D F14,-24(R1)
ADD.D F4,F0,F2
ADD.D F8,F6,F2
ADD.D F12,F10,F2
ADD.D F16,F14,F2
S.D 0(R1),F4
S.D -8(R1),F8
DADDUI R1,R1,#-32
S.D 16(R1),F12
BNE R1,R2,Loop
S.D 8(R1),F16

## Slide 57: Codes – After Scheduling
The execution time of the unrolled loop has dropped to 14 clock cycles
  3.5 cycles per element of the four
Compared with
  Unrolled but not scheduling: 7 cycles per element
  Scheduled but not unrolled: 6 cycles per element

## Slide 58: Summary of Loop Unrolling
The key is to know
  WHEN and HOW the ordering among instructions may be changed
  Register renaming + Instruction scheduling
  Instruction combination
In practice, this process must be performed in a methodical fashion by
  A compiler or (and)
  Hardware

## Slide 59: Homework
Textbook: 3.1-3.2
Papers
  "Performance from architecture: comparing a RISC and CISC with similar hardware organization", Bhandarkar, Clark, 1991
  "Architecture of the IBM System/360", Amdahl, Blaauw, Brooks, 1964