## Slide 1: Advanced Computer Architecture (ACA 2019)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2019

## Slide 2: Lecture 02 Instruction Set Architecture (ISA)
October 16, 2019

## Slide 3: Quiz 1 - Functions of X Y Z … 2min
X
Y
Z
X
Y
Z

## Slide 4: Coding
Memory
  32-bit address
  8-bit cell
Register
  32 32-bit
Program
  Add the number in memory address 0 and 1 to address 3
  Load r1, #0
  Load r2, #1
  Add r3, r1, r2
  Store r3, #3

## Slide 5: Objects Today
Storage
  Memory
  Regesters
Operands
Operations
Format of instructions
Addressing
Compiler

## Slide 6: What Is a Memory?
A container of binary number
How to specify a memory?
  How many binary cells (bits) can be accessed in one time? -- the object size
    8 bits in our book and most computer
    8 bits == a byte
  How many bytes in all? -- the memory size
  Where is the cell position? -- the address

## Slide 7: Accessing Mode
Bytes (8 bits)
Half words (16 bits)
Words (32 bits)
Double words (64 bits)
How to access these units?
  Programming in your code
  Test
  suggestion: in procedures

## Slide 8: The Little and Big Endian
bit | 0 | 7 | 8 | 15 | 16 | 23 | 24 | 31
 | byte #0 |  | byte #1 |  | byte #2 |  | byte #3 | 
 | 16-bit integer #0 |  |  |  | 16-bit integer #1 |  |  | 
 | 32-bit integer |  |  |  |  |  |  | 
0x | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
big-endian | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000
 | Most-S |  |  |  | Least-S |  |  | 
little-endian | Least-S |  |  |  | Most-S |  |  | 
 | 0111 | 1000 | 0101 | 0110 | 0011 | 0100 | 0001 | 0010

## Slide 9: Byte Aligned
An access to an object of size s bytes at byte address A is aligned if
A mod s = 0
  Figure A.5/page A8
Width of object | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Byte |  |  |  |  |  |  |  | 
Half word |  |  |  |  |  |  |  | 
Word |  |  |  |  |  |  |  | 
Double word |  |  |  |  |  |  |  | 

## Slide 10: Registers
Another forms of storage internal to the CPU
Three Types of Register File
  Accumulator architecture
  Stack architecture
  Register Architecture

## Slide 11: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Addressing
Format of instructions
Compiler

## Slide 12: Type and Size of Common Operands
Character | (1 byte)
Integer | Half word (16-bit short integer) Word (32-bit integer) Long word (64-bit integer)
Floating point (Real) | Word (32-bit single-precision number) Double word (64-bit double-precision number)
Decimal | Unpacked decimal A decimal characters string Packed decimal 4-bit to encode values 0-9, usually based on BCD code A two decimal digits packed into each byte

## Slide 13: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Addressing
Format of instructions
Compiler

## Slide 14: Operations: Types of Instructions
Operations | Examples
Arithmetic & logical | Integer: ADD, AND, OR, etc.
Data transfer | LOADS and STORES
Control | JUMP, CALL, RETURN TRAPS, etc.
System | OS call, virtual memory instructions
Floating point | Floating point: ADD, AND, OR, etc.
Decimal | Decimal: ADD, AND, conversion, etc.
String | String: MOVE, COMP, SEARCH, etc.
Graphics | Pixel operations, compression, etc.

## Slide 15: Top 10 Instructions for x86 (SPECint92)
Rank | 80x86 instruction | Integer average( % total executed)
1 | load | 22%
2 | conditional branch | 20%
3 | compare | 16%
4 | store | 12%
5 | add | 8%
6 | and | 6%
7 | sub | 5%
8 | move register-register | 4%
9 | call | 1%
10 | return | 1%
total |  | 96%

## Slide 16: Branch Instructions
Conditional branch -- branch
Unconditional branch -- jump
Call
Return

## Slide 17: The Frequencies of Control Flow Instructions

## Slide 18: Methods to Evaluation Branch Conditions
Name | How condition is tested
Condition code (CC) | Special bits are set by ALU operations
Condition register | Set arbitrary register with the result of a comparison
Compare and branch | Branch is part of the compare

## Slide 19: Branch Distances
Branch distances in terms of number of instructions between the target and the branch instruction

## Slide 20: Frequency of Conditional Branches

## Slide 21: Structure of a Copmuter
Storage
  Memory
  Registers
Operands
Operations
Addressing
Format of instructions
Compiler

## Slide 22: The Pop Addressing Modes
Addressing mode | Example instruction | Usage
Register | ADD R3,R4 | Value is in register
Immediate | ADD R4,#3 | Constants
Displacement | ADD R4,100(R1) | Local variables
Register indirect | ADD R4,(R1) | Pointers
Indexed | ADD R3,(R1+R2) | Array
Direct or absolute | ADD R1,(1001) | Static data
Mem. Indirect | ADD R1,@(R3) | Pointers
Auto increment | ADD R1,(R2)+ | Stepping
Auto decrement | ADD R1,-(R2) | As inc.
Scaled | ADD R1,100(R2)(R3) | To index array

## Slide 23: Immediate Operand
About one-quarter of data transfers and ALU operations have an immediate operand

## Slide 24: Immediate Values
16 bits would capture about 80% and 8 bits about 50% of immediates
  about 20% to 25% were longer than 16 bits

## Slide 25: Use of Memory Addressing Modes
Almost all the memory indirect references use displacement mode as the base
Displacement mode includes all displacement lengths (8, 16, and 32 bits)

## Slide 26: Displacement Values Distributions
These data were taken on the Alpha architecture with full optimization for SPEC CPU2000, showing the average of integer programs (CINT2000) and the average of floating-point programs (CFP2000)

## Slide 27: Structure of a Copmuter
Storage
  Memory
  Regesters
Operands
Operations
Addressing
Format of instructions
Compiler

## Slide 28: How to Encoding an Instruction Set
What fields must a instruction has?
How big the operations fields?
How many address fields must it has?
How long a address field ought to be?
Something else?

## Slide 29: Three Basic Variations in Instruction Encoding

## Slide 30: Reduced Code Size in RISCs
Several manufacturers offered a new hybrid version of their RISC instruction sets
  With both 16-bit and 32-bit instructions, even 64-bit
  The narrow instructions support
    Fewer operations
    Smaller address and immediate fields
    Fewer registers
    Two-address format

## Slide 31: Reduced Code Size in RISCs
The ARM Thumb and MIPS MIPS16, which both claim a code size reduction of up to 40%
  Instruction caches act as if they are about 25% larger
IBM's CodePack: compresses its standard instruction set
  An overall performance cost of 10%, resulting in a code size reduction of 35% to 40%
Hitachi invented a fixed 16-bit RISC instruction set, called SuperH

## Slide 32: A "Typical" RISC ISA
32-bit fixed format instruction
32 32-bit GPR (R0 == 0, DP takes pair)
3-address, reg-reg arithmetic instruction
Single address mode for load/store
Simple branch conditions
Delayed branch
SPARC, MIPS, HP PA, DEC Alpha, IBM PowerPC, CDC6600, CDC7600, Cray-1, Cray-2...

## Slide 33: Instruction Format
These four formats are found in all five architectures
  Op = the main opcode
  Opx = an opcode extension
  Rd = the destination register
  Rs1 = source register 1
  Rs2 = source register 2
  Const = a constant
    used as an immediate, address, mask, or sift amount

## Slide 34: Distribution of Data Accesses by Size

## Slide 35: Structure of a Copmuter
Storage
  Memory
  Regesters
Operands
Operations
Addressing
Format of instructions
Compiler

## Slide 36: The Structure of Compilers

## Slide 37: Major Types of Optimizations and Examples

## Slide 38: Change in ICs: Compiler Optimization Levels

## Slide 39: The Lineage of RISC Instruction Sets

## Slide 40: Berkeley New ISA, RISC-V
RISC-V is a new simple, clean, extensible ISA we developed at Berkeley for education and research
  RISC-I/II, Berkeley RISC implementations
  Berkeley research machines SOAR/SPUR considered RISC-III/IV
Both of the dominant ISAs (x86 and ARM) are too complex to use for teaching
RISC-V ISA manual available on web page
Full GCC-based tool chain available
Version 1.0 published on March 28, 2012

## Slide 41: Originator: Professor Krste Asanovic

## Slide 42: How Hot It Is?

## Slide 43: RISC-V Summit 2019

## Slide 44: The RISC-V Instruction Set Manual
RISC-V is a new ISA designed to support computer architecture research and education
Our goals in defining RISC-V include:
  Provide a realistic but open ISA that captures important details of commercial general-purpose ISA designs and that is suitable for direct hardware implementation.
  Provide a small but complete base ISA that avoids “over-architecting” for a particular microarchitecture style (e.g., microcoded, in-order, decoupled, out-of-order) or implementation technology (e.g., full-custom, ASIC, FPGA), but which allows efficient implementation in any of these
  Support both 32-bit and 64-bit address space variants for applications, operating system kernels, and hardware implementations.
  Support highly-parallel multicore or manycore implementations, including heterogeneous multiprocessors.
  Support an efficient dense instruction encoding with variable-length instructions, improving performance and reducing energy and code size.
  Support the revised 2008 IEEE 754 floating-point standard.
  Be fully virtualizable.
  Be simple to subset for educational purposes and to reduce complexity of bringing up new implementations.
  Support experimentation with user-level ISA extensions and specialized variants.
  Support independent experimentation with new supervisor-level ISA designs

## Slide 45: RISC-V ISA
New fifth-generation RISC design from UC Berkeley
Realistic & complete ISA, but open & small
Not over-architected for a certain implementation style
Both 32-bit (RV32) and 64-bit (RV64) address-space variants
Designed for multiprocessing
Efficient instruction encoding
Easy to subset/extend for education/research
Techreport with RISC-V spec available on class website
Increasing momentum with industry adoption

## Slide 46: RISC-V Has Three Base Instructions Sets

## Slide 47: RV32 Processor State
Program counter (pc)
32x32-bit integer registers (x0-x31)
x0 always contains a 0
32 floating-point (FP) registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fsr), used for FP rounding mode & exception reporting

## Slide 48: RISC-V Instruction Length Encoding
All the 32-bit instructions in the base ISA have their lowest two bits set to 11
The compressed 16-bit instruction-set extensions have their lowest two bits equal to 00, 01, or 10
Instruction-set extensions encoded with more than 32 bits have additional low-order bits set to 1

## Slide 49: RISC-V Dynamic Instruction for SPECint2006

## Slide 50: Reading – 10min Presentations
Textbook
  Appendix A
Two papers
  "The Case for the Reduced Instruction Set Computer", Patterson, Ditzel, 1980
  Comments on the "The Case for the RISC", Clark, Strecker, 1980
https://riscv.org/specifications/
  Two pages of ISA maps in educoder.net
Homeworks

## Slide 51: Next…
A Processor