## Slide 1: Advanced Computer Architecture (ACA 2019)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2019

## Slide 2: Lecture 04 pipelining problems

## Slide 3: Branch-Prediction Buffer (BPB)
The Simplest Dynamic Branch Prediction

## Slide 4: A General Dynamic Branch Prediction
Branch
Predictor
Incoming Branches
{ Address }
Prediction
{ Address, Value }
Corrections
{ Address, Value }
History
Information

## Slide 5: BPB Principles
 | Predictor 0
 | Predictor 1
lower | 
bits | 
of the | 
branch | 
PC | 
 | Predictor 2n-1

## Slide 6: 1-bit BPB Scheme
Prediction accuracy is about 80%
  Almost all loop will predict incorrectly twice

## Slide 7: 2-bit Scheme
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 8: BPB Prediction Accuracy
Accuracy: 4K-entry 2-bits BPB, SPEC89, IBM Power
  Accuracy: 82% ~ 99%
  Integer average 11%
    gcc, espresso, eqntott, li
  FP average 4%
    nasa7, matrix300, tomcatv
Why they are deference?

## Slide 9: Mispredictions
Chart: 4K-entry 2-bits BPB for SPEC89 (IBM Power)
| nasa7 | matrix300 | tomcatv | doduc | spice | fpppp | gcc | espresso | entott | li
mispredictions | 0.01 | 0 | 0.01 | 0.05 | 0.09 | 0.09 | 0.12 | 0.05 | 0.18 | 0.1

## Slide 10: The 2-bit Scheme: an Alternative
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 11: Entries Mis : 4K vs. Unlimited, 2bit/entry
Chart: 
| nasa7 | matrix300 | tomcatv | doduc | spice | fpppp | gcc | espresso | eqntott | li
4096-entry:2-bit/entry | 0.01 | 0 | 0.01 | 0.05 | 0.09 | 0.09 | 0.12 | 0.05 | 0.18 | 0.1
Unlimited entries: 2-bit/entry | 0 | 0 | 0 | 0.05 | 0.09 | 0.09 | 0.11 | 0.05 | 0.18 | 0.1

## Slide 12: BPB: Typical Implementations
As a “cache”
Accessed with the instruction address during the IF
  Taken -> fetching begins from the target as soon as the PC is known
  Not taken -> sequential fetching continues

## Slide 13: BPB: an Instruction Address
0
0
Fetch PC

## Slide 14: BPB: IFatch and 2k 2 bits Predicter Select
0
0
Fetch PC
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 15: BPB: Decode & Target PC
2K-entry BPB, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 16: Precise Piplining Problems
Next ...

## Slide 17: Exception
Exception cover fault and exception
Page C-38 to C-43

## Slide 18: Problem
It must appear between 2 instructions (Ii and Ii+1)
  Up to and including Ii must complete
  No effect after Ii
Handler
  aborts
  restarts at instruction Ii+1
Safe？

## Slide 19: Precise Exceptions
stopped just before the faulting instruction are completed
  those after it can be restarted from scratch
modern processor must make its exceptions precise
  Why?

## Slide 20: Exceptions May in the RISC V Pipeline
Pipeline stage | Problem exceptions occurring
IF | Page fault on instruction fetch; Misaligned memory access; Memory protection violation
ID | Undefined or illegal opcode
EX | Arithmetic exception
MEM | Page fault on data fetch; Misaligned memory access; Memory protection violation
WB | None

## Slide 21: Multicycle Operations
Next ...

## Slide 22: Four Separate FUs

## Slide 23: Latency and Initiation Interval
Functional unit | Latency | Initiation interval
Integer ALU | 0 | 1
Data memory (int & FP loads) | 1 | 1
FP add | 3 | 1
FP multiply (also int. multiply) | 6 | 1
FP divide (also integer divide) | 24 | 25

## Slide 24: The Multiple Pipelines

## Slide 25: Stalls per FP Operation for SPEC89 FP

## Slide 26: The stalls for FP pipeline for SPEC89 FP

## Slide 27: Scoreboard
Dynamically Scheduled Pipelines

## Slide 28: CDC 6600: designed by Seymore Cray
Control Data Corporation, CEO, William Norris
CDC 6600 Released: 1964
  Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)
OS: COS, SCOPE, MACE, KRONOS
Processor: One 60-bit CPU
  The fastest clock speed for its day (100 ns, 10Mhz)
  FP add in 4 clocks
  Memory: 128K 60-bit words
  Ten shared-logic 12-bit peripheral I/O processors
  Display: Printer, plotter and dual video display console
  Storage: 2MB extended core storage, magnetic disk, magnetic drum
  400,000 transistors
  Over 100 miles of wiring (done by hand)
  Freon refrigerant cooling

## Slide 29: Some Photos (from Internet)

## Slide 30: IBM Internal Memo
"Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer."
  Thomas Watson Jr., IBM CEO, August 1963
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 31: Review: Scoreboard (CDC 6600)
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 32: Scoreboard Implications
Solutions for WAR
  Stall writeback until registers have been read
  Read registers only during Read Operands stage
Solution for WAW
  Detect hazard and stall issue of new instruction until other instruction completes
Need to have multiple instructions in execution phase
  => multiple execution units or pipelined execution units

## Slide 33: The 1st Stages: Issue
Issue -- Decode instructions & check for structural hazards (ID1)
  Instructions issued in program order (for hazard checking)
  Don’t issue if structural hazard
  Don’t issue if instruction is output dependent on any previously issued but uncompleted instruction (no WAW hazards)

## Slide 34: The 2nd Stages: Read Operands
Read Operands -- Wait until no data hazards, then read operands (ID2)
  All real dependencies resolved in this stage, since we wait for instructions to write back data (RAW hazards)
  No forwarding of data in this model !
    Data can not be used until in registers

## Slide 35: The 3rd Stages: Execution
Execution -- operate on operands (EX)
  The functional unit begins execution upon receiving operands
  When the result is ready, it notifies the scoreboard that it has completed execution

## Slide 36: The 4th Stages: Write Result
Write result -- finish execution (WB)
  Stall until no WAR hazards with previous instructions

## Slide 37: Three Parts of the Scoreboard
Instruction status
  Which of 4 steps the instruction is in
Register result status
  Indicates which functional unit will write each register, if one exists
  Blank when no pending instructions will write that register
Functional unit status
  Indicates the state of the FU
  9 fields for each functional unit
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 38: 9 Fields for Each Functional Unit
Busy: Indicates the unit is busy or not
Op: Operation to perform in the unit (e.g., + or –)
Fi: Destination register
Fj, Fk: Source-register numbers
Qj, Qk: Functional units producing source registers Fj, Fk
Rj, Rk: Flags indicating when Fj, Fk are ready
Notes: What you might have thought
1. 4 stages of instruction execution
2. Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 39: How It Works
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 40: Where Are the RAWs?
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 41: RAWs
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 42: Where WARs?
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 43: WARs
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 44: EX Cycle Latencies
EX cycle latencies for the FP function units
  ADD is 2 clock cycles
  MULTIPLY is 10 cycles
  DIVIDE is 40 cycles

## Slide 45: Scoreboard Example

## Slide 46: Scoreboard Example: Cycle 1
Notes: 三个表三个类

## Slide 47: Scoreboard Example: Cycle 2

## Slide 48: Scoreboard Example: Cycle 2
Issue 2nd LD?

## Slide 49: Scoreboard Example: Cycle 3

## Slide 50: Scoreboard Example: Cycle 3
Issue MULT?

## Slide 51: Scoreboard Example: Cycle 4
Notes: 第四个时钟结束后，该LD指令结束了
即Interger指令不处于busy状态？？

## Slide 52: Scoreboard Example: Cycle 5
Notes: 第五个时钟到来时，第二个Integer指令被发射，而且此时的Rk寄存器是可以进行读数的，而且此时也没有来自生产所需寄存器的功能单元的限制，
于是下一个时钟会对应着读入操作数。

## Slide 53: Scoreboard Example: Cycle 6
Notes: 在第六个时钟到来的时刻，第二个指令集对应的FU开始读入操作数，而且第三个指令开始issue，但此时该乘法指令还在等待第二个Integer指令的结果写入，
导致该乘法指令不能在下一时钟进行读数，所以将处于stall状态。

## Slide 54: Scoreboard Example: Cycle 7
Notes: Cycle7：
第二个指令进入到操作阶段，对应的功能单元开始进行运算，并且此时由于已经从R3中读完数据，所以对应的ready状态由yes到no（这是默认的）
由于integer功能单元还未将结果写入到F2中，所以第三个指令仍是处于stall状态
第四个指令此时发射，但由于第二个操作数所处的寄存器还需要等待第二个指令集写入后的结果，所以不能读出F2寄存器所对应的值，为了避免RAW冒险，
所以出于stall状态。

## Slide 55: Scoreboard Example: Cycle 7
Read multiply operands?

## Slide 56: Cycle 8a (First half of clock)
Read operands for MULT & SUB?
Notes: Cycle8：
在前半个时钟内： 在第二个指令对应的FU没有将结果写入F2前不得从中读取数据即：第三条指令继续暂停，第四条也如此；
第五条指令进行发射，但由于第一个操作数所在的F0寄存器是需要等待第三个指令集所对应FU将结果写入到F0寄存器中，
所以下一时钟第五个FU将处于stall状态

## Slide 57: Cycle 8b (Second half of clock)
Notes: Cycle8：
在后半个时钟内：
F2的数据写入完毕，指令集处于not busy状态
第三个和第四个指令集进入到读数阶段，对应的乘法和加法FU也能分别从F2，F4和F6，F2中读取数据；

## Slide 58: Scoreboard Example: Cycle 9
Note
Remaining
Notes: cycle9算是读入数据，之后从cycle10开始就算是延迟了

## Slide 59: Scoreboard Example: Cycle 9
Issue ADDD?
Note
Remaining
Self learning
Notes: Cycle9： 由于第五个除法指令集所对应的FU的第一个操作数是需要从第三个指令集对应的乘法FU的写出结果中读取的，所以处于stall状态
此时第三个指令集将进入执行阶段，注意此时还需要10个cycle来完成这个部分。
此时第四个指令集也完成了读数阶段，之后还需要2个cycle来完成接下来的加法操作。？？？ 应该是说到执行阶段会存在10个，2个延迟吧？那具体到物理过程是什么，各类触发器所导致的延时，那运算就不需要么

## Slide 60: Scoreboard Example: Cycle 10
Self learning
Notes: Cycle10：
完成读数阶段后，对应的源寄存器的状态设为no
此时除法指令集对应FU还是处于stall状态

## Slide 61: Scoreboard Example: Cycle 11
Self learning
Notes: cycle11：
第九个时钟结束后的第二个时钟完成之时，第四个指令集对应的FU，完成了其读数操作，进入到了执行阶段，

## Slide 62: Scoreboard Example: Cycle 12
Self learning
Notes: cycle12：
一旦进入到WR阶段，指令集的Busy状态为No，

## Slide 63: Scoreboard Example: Cycle 12
Read operands for DIVD?
Issue ADDD?
Self learning

## Slide 64: Scoreboard Example: Cycle 13
Self learning

## Slide 65: Scoreboard Example: Cycle 14
Self learning

## Slide 66: Scoreboard Example: Cycle 15
Self learning

## Slide 67: Scoreboard Example: Cycle 16
Self learning

## Slide 68: Scoreboard Example: Cycle 17
Self learning

## Slide 69: Scoreboard Example: Cycle 17
Why not write result of ADDD?
Self learning

## Slide 70: Scoreboard Example: Cycle 17
Why not write result of ADDD?
WAR Hazard!
Self learning

## Slide 71: Scoreboard Example: Cycle 18
Self learning

## Slide 72: Scoreboard Example: Cycle 19
Self learning
Notes: 在从源寄存器中读取数据后的第十个时钟内，乘法指令对应FU进入到了执行阶段，对应其他FU的源寄存器标签马上随之变化

## Slide 73: Scoreboard Example: Cycle 20
Self learning
Notes: 到cycle20时，乘法指令集进入到WR状态，那么此cycle结束时，对应的指令停止发射，

## Slide 74: Scoreboard Example: Cycle 21
Self learning
Notes: cycle21 则是消除RAW冒险后的第一个时钟，那么此时除法FU进入到读数阶段

## Slide 75: Scoreboard Example: Cycle 21
WAR Hazard is now gone...
Self learning
Notes: 读数之后是40个时钟的延迟

## Slide 76: Scoreboard Example: Cycle 22
Self learning
Notes: 在cycle22时，除法FU已经读取了源寄存器的数据，那么对应的加法FU可以在该时钟周期内完成其WR过程

## Slide 77: Faster than light computation
(skip a couple of cycles)
Self learning

## Slide 78: Scoreboard Example: Cycle 61
Self learning

## Slide 79: Scoreboard Example: Cycle 62
Self learning

## Slide 80: Review: Scoreboard Status

## Slide 81: Review: Scoreboard Status
In-order issue
Out-of-order execute
Out-of-order WR

## Slide 82: Issue
not Busy[FU] and not Result [D]
Bookkeeping
  Busy[FU]  yes; OP[FU]  Op;
  Fi[FU]  D; Fj[FU]  S1; Fk[FU]  S2;
  Qj  Result[S1]; Qk  Result[S2];
  Rj  not Qj; Rk  not Qk;
  Result[D]  FU;
Self learning

## Slide 83: Read operands
Rj and Rk
    //operands are ready, check RAW
Bookkeeping
  Rj  No; Rk  No;
    //Rj, Rk have been used
  Qj  0; Qk  0;
    //no FU results are waited
Self learning

## Slide 84: Execution
Execution complete
  Functional unit done
Self learning

## Slide 85: Write Result
Wait until f((Fj[f]  Fi[FU] or Rj[f] = no) & (Fk[f]  Fi[FU] or Rk[f] = no));
Bookkeeping
  f(if Qj[f] = FU then Rj[f]  yes);
    //all Fjs are OK
  f(if Qk[f] = FU then Rk[f]  yes);
    //all Fks are OK
  Result [Fi[FU]]  0;
  Busy[FU]  No;
Self learning

## Slide 86: Scoreboard on the CDC 6600
CDC 6600
  No software pipeline scheduling
  No semiconductor main memory
  No caches (lower memory-access time)
Cost of scoreboard on the CDC 6600 is surprisingly low
  About as much logic as one of the FU
  The main cost is large number of buses (data trunk) that is about four times as many as executing in order

## Slide 87: The CDC6600 Benefits
Improvement | Cede Type
1.7 | FORTRAN
2.5 | hand-coded assembly

## Slide 88: Limitations of 6600 Scoreboard
No forwarding hardware
Limited to instructions in basic block
  Small window
Small number of functional units
  Structural hazards
  Especially integer/load store units
Do not issue on structural hazards
Wait for WAR hazards
Prevent WAW hazards

## Slide 89: Summary
Hazards limit performance
  Structural: need more HW resources
  Data: need forwarding, compiler scheduling
  Control: early evaluation & PC, delayed branch, prediction
ILP found either by compiler or hardware
Increasing length of pipe increases impact of hazards
  Pipelining helps instruction bandwidth, not latency!

## Slide 90: Ambitiously
Missing from 6600 Scoreboard?
  Hardware renaming – name dependencies limiting our potential speedup on loops!
    Can we rename in hardware? Of course – next time
  Concurrent write result to destination register and read operands

## Slide 91: Historical View: Pipelining Tech
At the 1980s, for
  Supercomputers
  Large multimillion dollar mainframes
By the mid-1980s
  The first pipelined microprocessors
  Microprocessors bypass minicomputers and mainframes
By the early 1990s
  High-end embedded microprocessors
  Desktops were dynamically scheduled, multiple-issue

## Slide 92: Homework
Read C7
  Algorithm and write the functional explanation to each statement (operation and result)
Project:
  RISC V subset selection
    For one week
  Coding for scoreboard
    The proposals must submitted in two weeks

## Slide 93: Next…
ILP