## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 03 Instruction Set Simple Implementations

## Slide 3
Papers reading
The 1st
The 2nd
The 3rd
Questions?
A
B
C
D
Submit
Poll
1 answer(s) at most

## Slide 4: Berkeley RISC Chips
RISC-I (1982)
  Contains 44,420 transistors
  Fabbed in 5 µm NMOS, ran at 1 MHz with a die area of 77 mm2
  This chip is probably the first VLSI
RISC RISC-II (1983)
  Contains 40,760 transistors
  Fabbed in 3 µm NMOS, ran at 3 MHz, and the die size is 60 mm2

## Slide 6: Big PIC of RISC II

## Slide 7: Fields of all Instructions
Operation
Operands
  Operand 1
  Operand 2
  Operand 3

## Slide 8: Instruction Execution Phases
Instruction Fetch
Instruction Decode
Register Fetch
ALU Operations
Optional Memory Operations
Optional Register Writeback
Calculate Next Instruction Address

## Slide 9: 5 Phrases of Datapath
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
L
M
D
ALU
MUX
Memory
Reg File
Data
Memory
Sign
Extend
4
Adder
Zero?
Next SEQ PC
Address
Next PC
WB Data
Inst
RD
RS1
RS2
Imm
IR <= mem[PC];
PC <= PC + 4
Reg[IRrd] <= Reg[IRrs] opIRop Reg[IRrt]
MUX
MUX
MUX

## Slide 10: Inst. Processing
Ifetch
    Mem <= [PC]
    IR <= mem[PC];
    PC <= PC + 4
opFetch-DCD
    A <= Reg[IRrs];
    B <= Reg[IRrt]
  Br
    if bop(A,b)
      PC <= PC+IRim
  J
    PC <= IRjaddr
  RR
    r <= A opIRop B
    WB <= r
    Reg[IRrd] <= WB
  RI
    r <= A opIRop IRim
    WB <= r
    Reg[IRrd] <= WB
  LD(ST)
    r <= A + IRim
    WB <= Mem[r]
    Reg[IRrd] <= WB

## Slide 11: Pipelined Datapath : Original
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Ext
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we

## Slide 12: Pipelined with Latches and Stages
write
-back
phase
fetch
phase
execute
phase
decode & Reg-fetch
phase
memory
phase
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Ext
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
IR
PC
Clock period can be reduced by dividing the execution of an instruction into multiple cycles
tC > max {tIM, tRF, tALU, tDM, tRW} (= tDM probably)

## Slide 13: Hazards
Next

## Slide 14: Limits to pipelining: Hazards and Types
HAZARDS prevent next instruction from executing during its designated clock cycle
Three classes of hazards
  STRUCTURAL hazards
  DATA hazards
  CONTROL hazards

## Slide 15: Structural Hazards: One Port Mem.
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 16: Structural Hazards: Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 17: Data Hazard on R1
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 18: Types of Data Hazards
RESULTS depends on in the pipeline
  Read after write
  Write after read
  Write after write
  Read after read (?)

## Slide 19: Data Hazards of “r1”
Read After Write (RAW)
  I: add r1,r2,r3
  J: sub r4,r1,r3
Write After Read (WAR)
  I: sub r4,r1,r3
  J: add r1,r2,r3
Write After Write (WAW)
  I: sub r1,r4,r3
  J: add r1,r2,r3

## Slide 20: Forwarding to Avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 21: HW Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux

## Slide 22: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 23: Data Hazard Even with Forwarding
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg

## Slide 24: The Revised Pipelined
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 25: Branch Penalties
Next…

## Slide 26: Four Branch Hazard Alternatives
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
#3: Predict Branch Taken
#4: Delayed Branch

## Slide 27: Untaken and Taken in a Predicted-not-taken
untaken
taken

## Slide 28: The Behavior of A Delayed Branch
untaken
taken

## Slide 29: The Simplest Scheme: Predict as TAKEN
Average misprediction rate
  TAKEN = UNTAKEN
  For the SPEC programs is 34%
The misprediction rate for the SPEC ranges
  From not very accurate (59%) to highly accurate (9%)

## Slide 30: Direction-based Prediction
Predict on the basis of branch direction
  Backward-going branches to be TAKEN
  Forward-going branches to be NOT TAKEN
  Misprediction rate: 30% ~ 40%
An enhanced direction-based prediction
  Uses program context information
    Using previous branch information

## Slide 31: Profile-based Prediction
Predict branches on the basis of profile information collected from earlier runs
  An individual branch is often highly biased toward taken or untaken
  INPUT sensitive
Varies widely
  The FP, an average rate of 9% with a standard deviation of 4%
  The integer, an average rate of 15% with a standard deviation of 5%

## Slide 32: Profile-based Predictor : Misprediction
Chart: 
| Compress | eqntott | espresso | gcc | li | doduc | era | hydro2d | mdljdp | su2cor
Misprediction rate | 0.12 | 0.22 | 0.18 | 0.11 | 0.12 | 0.05 | 0.06 | 0.09 | 0.1 | 0.15

## Slide 33: Instructions Between Misprediction
Chart: 
| Compress | eqntott | espresso | gcc | li | doduc | era | hydro2d | mdljdp | su2cor
Predicted taken | 10 | 6 | 11 | 11 | 14 | 19 | 11 | 11 | 14 | 96
Profile based | 56 | 19 | 37 | 60 | 58 | 250 | 159 | 92 | 113 | 253

## Slide 34: Next …
The Simplest Dynamic Branch Prediction – Branch-Prediction Buffer (BPB)

## Slide 35: A General Dynamic Branch Prediction
Branch
Predictor
Incoming Branches
{ Address }
Prediction
{ Address, Value }
Corrections
{ Address, Value }
History
Information

## Slide 36: BPB Principles
 | Predictor 0
 | Predictor 1
lower | 
bits | 
of the | 
branch | 
PC | 
 | Predictor 2n-1

## Slide 37: 1-bit BPB Scheme
Prediction accuracy is about 80%
  Almost all loop will predict incorrectly twice

## Slide 38: 2-bit Scheme
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 39: BPB Prediction Accuracy
Accuracy: 4K-entry 2-bits BPB, SPEC89, IBM Power
  Accuracy: 82% ~ 99%
  Integer average 11%
    gcc, espresso, eqntott, li
  FP average 4%
    nasa7, matrix300, tomcatv
Why they are deference?

## Slide 40: Mispredictions
Chart: 4K-entry 2-bits BPB for SPEC89 (IBM Power)
| nasa7 | matrix300 | tomcatv | doduc | spice | fpppp | gcc | espresso | entott | li
mispredictions | 0.01 | 0 | 0.01 | 0.05 | 0.09 | 0.09 | 0.12 | 0.05 | 0.18 | 0.1

## Slide 41: The 2-bit Scheme: an Alternative
Predict taken
11
Predict not taken
01
Predict not taken
00
Predict taken
10
Taken
Taken
Not taken
Taken
Not taken
Not taken
Not taken
Taken

## Slide 42: Entries Mis : 4K vs. Unlimited, 2bit/entry
Chart: 
| nasa7 | matrix300 | tomcatv | doduc | spice | fpppp | gcc | espresso | eqntott | li
4096-entry:2-bit/entry | 0.01 | 0 | 0.01 | 0.05 | 0.09 | 0.09 | 0.12 | 0.05 | 0.18 | 0.1
Unlimited entries: 2-bit/entry | 0 | 0 | 0 | 0.05 | 0.09 | 0.09 | 0.11 | 0.05 | 0.18 | 0.1

## Slide 43: Next: BPB
A Faster Branch Prediction Processing

## Slide 44: BPB: Typical Implementations
As a “cache”
Accessed with the instruction address during the IF
Attached to instruction cache
If the instruction is decoded as a branch -> the bits fetched predict it as
  Taken -> fetching begins from the target as soon as the PC is known
  Not taken -> sequential fetching continues

## Slide 45: BPB: an Instruction Address
0
0
Fetch PC

## Slide 46: BPB: IFatch and 2k 2 bits Predicter Select
0
0
Fetch PC
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 47: BPB: Decode & Target PC
2K-entry BPB, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BPB Index
2k-entry
BPB,
2 bits/entry
Taken/¬Taken?

## Slide 48: Next ...
Piplining Problems

## Slide 49: Exception and Interrupt
Exception
  An unusual event happens to an instruction during its execution
  Examples: divide by zero, undefined opcode
Interrupt
  Hardware signal to switch the processor to a new instruction stream
  Example: a key pressed

## Slide 50: Problem
It must appear that the exception or interrupt must appear between 2 instructions (Ii and Ii+1)
  The effect of all instructions up to and including Ii is totally complete
  No effect of any instruction after Ii can take place
The interrupt (exception) handler either aborts program or restarts at instruction Ii+1

## Slide 51: Safely Steps
Force a trap instruction into the pipeline on the next IF
Until the trap is taken, turn off all writes for the faulting instruction
The following exception-handling routine immediately saves the PC of the faulting instruction

## Slide 52: Precise Exceptions
If the pipeline can be stopped just before the faulting instruction are completed and those after it can be restarted from scratch
Any processor with demand paging or IEEE arithmetic trap handlers must make its exceptions precise

## Slide 53: Next ...
Multicycle Operations

## Slide 54: Four Separate FUs In Our MIPS

## Slide 55: Latency and Initiation Interval
Functional unit | Latency | Initiation interval
Integer ALU | 0 | 1
Data memory (int & FP loads) | 1 | 1
FP add | 3 | 1
FP multiply (also int. multiply) | 6 | 1
FP divide (also integer divide) | 24 | 25

## Slide 56: The Pipelines

## Slide 57: How Big a Chip

## Slide 58: John L. Hennessy
John Hennessy served as Stanford's tenth president from 2000 – 2016
Stanford MIPS processor

## Slide 59: Homeworks
Book reading
  Appendix C
Reading papers
  Performance from architecture: comparing a RISC and CISC with similar hardware organization, Bhandarkar, Clark, 1991
  Implementation of Precise Interrupts in Pipelined Processors, James E. Smith, Andrew R. Pleszkun, 1985
Open question: topic of next week
  If you implement the RISC-V, which instructions will you select?
  Why?

## Slide 60: Next…
Scoreboarding