## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Scoreboard
Dynamically Scheduled Pipelines

## Slide 3: CDC 6600: designed by Seymore Cray
Control Data Corporation, CEO, William Norris
CDC 6600 Released: 1964
  Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)
OS: COS, SCOPE, MACE, KRONOS
Processor: One 60-bit CPU
  The fastest clock speed for its day (100 ns, 10Mhz)
  FP add in 4 clocks
  Memory: 128K 60-bit words
  Ten shared-logic 12-bit peripheral I/O processors
  Display: Printer, plotter and dual video display console
  Storage: 2MB extended core storage, magnetic disk, magnetic drum
  400,000 transistors
  Over 100 miles of wiring (done by hand)
  Freon refrigerant cooling

## Slide 4: Some Photos (from Internet)

## Slide 5: IBM Internal Memo
"Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer."
  Thomas Watson Jr., IBM CEO, August 1963
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 6: Review: Scoreboard (CDC 6600)
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD
Notes: FP 浮点数

## Slide 7: Scoreboard Implications
Solutions for WAR
  Stall writeback until registers have been read
  Read registers only during Read Operands stage
Solution for WAW
  Detect hazard and stall issue of new instruction until other instruction completes
Need to have multiple instructions in execution phase
  => multiple execution units or pipelined execution units

## Slide 8: The 1st Stages: Issue
Issue -- Decode instructions & check for structural hazards (ID1)
  Instructions issued in program order (for hazard checking)
  Don’t issue if structural hazard
  Don’t issue if instruction is output dependent on any previously issued but uncompleted instruction (no WAW hazards)

## Slide 9: The 2nd Stages: Read Operands
Read Operands -- Wait until no data hazards, then read operands (ID2)
  All real dependencies resolved in this stage, since we wait for instructions to write back data (RAW hazards)
  No forwarding of data in this model !
    Data can not be used until in registers

## Slide 10: The 3rd Stages: Execution
Execution -- operate on operands (EX)
  The functional unit begins execution upon receiving operands
  When the result is ready, it notifies the scoreboard that it has completed execution

## Slide 11: The 4th Stages: Write Result
Write result -- finish execution (WB)
  Stall until no WAR hazards with previous instructions

## Slide 12: Three Parts of the Scoreboard
Instruction status
  Which of 4 steps the instruction is in
Register result status
  Indicates which functional unit will write each register, if one exists
  Blank when no pending instructions will write that register
Functional unit status
  Indicates the state of the FU
  9 fields for each functional unit
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 13: 9 Fields for Each Functional Unit
Busy: Indicates the unit is busy or not
Op: Operation to perform in the unit (e.g., + or –)
Fi: Destination register
Fj, Fk: Source-register numbers
Qj, Qk: Functional units producing source registers Fj, Fk
Rj, Rk: Flags indicating when Fj, Fk are ready
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 14: How It Works
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 15: Where Are the RAWs?
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 16: RAWs
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 17: Where WARs?
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 18: WARs
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 19: EX Cycle Latencies
EX cycle latencies for the FP function units
  ADD is 2 clock cycles
  MULTIPLY is 10 cycles
  DIVIDE is 40 cycles

## Slide 20: Scoreboard Example

## Slide 21: Scoreboard Example: Cycle 1

## Slide 22: Scoreboard Example: Cycle 2

## Slide 23: Scoreboard Example: Cycle 2
Issue 2nd LD?

## Slide 24: Scoreboard Example: Cycle 3

## Slide 25: Scoreboard Example: Cycle 3
Issue MULT?
Notes: 上一条指令没有发出，则当前指令不发出？

## Slide 26: Scoreboard Example: Cycle 4

## Slide 27: Scoreboard Example: Cycle 5

## Slide 28: Scoreboard Example: Cycle 6

## Slide 29: Scoreboard Example: Cycle 7

## Slide 30: Scoreboard Example: Cycle 7
Read multiply operands?

## Slide 31: Cycle 8a (First half of clock)
Read operands for MULT & SUB?

## Slide 32: Cycle 8b (Second half of clock)
Notes: 一拍拆成了两半，前一半写寄存器，后一半写。。。

## Slide 33: Scoreboard Example: Cycle 9
Note
Remaining
Notes: 附加计数器，记录乘法的进行情况

## Slide 34: Scoreboard Example: Cycle 9
Issue ADDD?
Note
Remaining
Self learning
Notes: Functional unit add只有一个

## Slide 35: Scoreboard Example: Cycle 10
Self learning

## Slide 36: Scoreboard Example: Cycle 11
Self learning

## Slide 37: Scoreboard Example: Cycle 12
Self learning

## Slide 38: Scoreboard Example: Cycle 12
Read operands for DIVD?
Issue ADDD?
Self learning

## Slide 39: Scoreboard Example: Cycle 13
Self learning

## Slide 40: Scoreboard Example: Cycle 14
Self learning

## Slide 41: Scoreboard Example: Cycle 15
Self learning

## Slide 42: Scoreboard Example: Cycle 16
Self learning

## Slide 43: Scoreboard Example: Cycle 17
Self learning

## Slide 44: Scoreboard Example: Cycle 17
Why not write result of ADDD?
Self learning

## Slide 45: Scoreboard Example: Cycle 17
Why not write result of ADDD?
WAR Hazard!
Self learning

## Slide 46: Scoreboard Example: Cycle 18
Self learning

## Slide 47: Scoreboard Example: Cycle 19
Self learning

## Slide 48: Scoreboard Example: Cycle 20
Self learning

## Slide 49: Scoreboard Example: Cycle 21
Self learning

## Slide 50: Scoreboard Example: Cycle 21
WAR Hazard is now gone...
Self learning

## Slide 51: Scoreboard Example: Cycle 22
Self learning

## Slide 52: Faster than light computation
(skip a couple of cycles)
Self learning

## Slide 53: Scoreboard Example: Cycle 61
Self learning

## Slide 54: Scoreboard Example: Cycle 62
Self learning
Notes: 指令顺序流出，乱序结束

## Slide 55: Review: Scoreboard Status

## Slide 56: Review: Scoreboard Status
In-order issue
Out-of-order execute
Out-of-order WR

## Slide 57: Issue
not Busy[FU] and not Result [D]
Bookkeeping
  Busy[FU]  yes; OP[FU]  Op;
  Fi[FU]  D; Fj[FU]  S1; Fk[FU]  S2;
  Qj  Result[S1]; Qk  Result[S2];
  Rj  not Qj; Rk  not Qk;
  Result[D]  FU;
Self learning

## Slide 58: Read operands
Rj and Rk
    //operands are ready, check RAW
Bookkeeping
  Rj  No; Rk  No;
    //Rj, Rk have been used
  Qj  0; Qk  0;
    //no FU results are waited
Self learning

## Slide 59: Execution
Execution complete
  Functional unit done
Self learning

## Slide 60: Write Result
Wait until f((Fj[f]  Fi[FU] or Rj[f] = no) & (Fk[f]  Fi[FU] or Rk[f] = no));
Bookkeeping
  f(if Qj[f] = FU then Rj[f]  yes);
    //all Fjs are OK
  f(if Qk[f] = FU then Rk[f]  yes);
    //all Fks are OK
  Result [Fi[FU]]  0;
  Busy[FU]  No;
Self learning

## Slide 61: Scoreboard on the CDC 6600
CDC 6600
  No software pipeline scheduling
  No semiconductor main memory
  No caches (lower memory-access time)
Cost of scoreboard on the CDC 6600 is surprisingly low
  About as much logic as one of the FU
  The main cost is large number of buses (data trunk) that is about four times as many as executing in order

## Slide 62: The CDC6600 Benefits
Improvement | Cede Type
1.7 | FORTRAN
2.5 | hand-coded assembly

## Slide 63: Limitations of 6600 Scoreboard
No forwarding hardware
Limited to instructions in basic block
  Small window
Small number of functional units
  Structural hazards
  Especially integer/load store units
Do not issue on structural hazards
Wait for WAR hazards
Prevent WAW hazards

## Slide 64: Summary
Hazards limit performance
  Structural: need more HW resources
  Data: need forwarding, compiler scheduling
  Control: early evaluation & PC, delayed branch, prediction
ILP found either by compiler or hardware
Increasing length of pipe increases impact of hazards
  Pipelining helps instruction bandwidth, not latency!

## Slide 65: Ambitiously
Missing from 6600 Scoreboard?
  Hardware renaming – name dependencies limiting our potential speedup on loops!
    Can we rename in hardware? Of course – next time
  Concurrent write result to destination register and read operands

## Slide 66: Historical View: Pipelining Tech
At the 1980s, for
  Supercomputers
  Large multimillion dollar mainframes
By the mid-1980s
  The first pipelined microprocessors
  Microprocessors bypass minicomputers and mainframes
By the early 1990s
  High-end embedded microprocessors
  Desktops were dynamically scheduled, multiple-issue

## Slide 67: Homework
Read C7
  Algorithm and write the functional explanation to each statement (operation and result)
Project:
  Coding for scoreboard
    The proposals submitted in two weeks

## Slide 68: Next…
Branches