## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 08 Multiple Issue

## Slide 3: Super Scale
3.7 Multiple-issue

## Slide 4: Superscalar – HiStory
IBM pioneering work: John Cocke
  ASC, A eventually canceled 1960’s project: follow Stretch (the first general-purpose pipelined processor, the IBM 7030) and surpass the CDC 6600/6800
  An mid-1980s research processor: “America”, coined the term superscalar
  The1989 Power-1 of RS/6000 was the first to use this approach
Today practically all RISC like processors use superscalar
  Issue a small number (1~8) of instructions per cycle

## Slide 5: Five Primary Approaches for Multiple-issue
Common name | Issue structure | Hazard detection | Scheduling | Distinguishing characteristic | Examples
Superscalar (static) | dynamic | hardware | static | in-order execution | Sun UltraSPARC II/III
Superscalar (dynamic) | dynamic | hardware | dynamic | some out-of-order execution | IBM Power2
Superscalar (speculative) | dynamic | hardware | dynamic with speculation | out-of-order execution with speculation | Intel P4, i3/i5/i7, MIPS R10K IBM Power6
VLIW/LIW | static | software | static | no hazards between issue packets | Trimedia, i860
EPIC | mostly static | mostly software | mostly static | explicit dependences marked by compiler | Itanium

## Slide 6: Statically-scheduled Superscalar
Instructions issue in order
All pipeline hazards are checked
  At issue time
  By the pipeline control logic
  Among the instructions being issued in a given clock cycle
  Among the issuing instructions all still in execution

## Slide 7: Issue Packet
During instruction fetch the pipeline would receive a group of instructions (the issue packet) from the IF unit
  It could potentially issue in one clock cycle
The ISSUE (dispatch) unit EXAMINES each instruction in the issue packet in program order

## Slide 8: Issue Checks
Sufficiently complex
  Performing them in one cycle means the issue logic is the minimum clock length
  Instruction issue is likely to be one limitation on the clock rate
Many statically and all dynamically scheduled superscalars split and pipelined issue stage
  Less obvious how to pipeline it further

## Slide 9: Superscalar Issue: Instructions Check
Each issued instruction must check against W*L instructions, i.e., growth in hardware  W*(W*L)
Lifetime L
Issue Group
Previously Issued Instructions
Issue Width W

## Slide 10: Superscalar Control Logic Scaling
L is related to all still lived instructions
  For in-order machines, L is related to pipeline latencies
  For out-of-order machines, L also includes time spent in instruction buffers (instruction window or ROB)
As W increases, larger instruction window is needed to find enough parallelism to keep machine busy => greater L
  o-o-o control logic grows faster than W2 (~W3)

## Slide 11: Our Two Issued Statically Superscalar MIPS
One INT instruction can be
  A load
  A store
  A branch, or
  A integer ALU operation
The other can be any FP operation
  Very close to HP 7100
  Like Intel Pentium (80586)

## Slide 12: Instructions Fetching
Fetching and decoding 64 bits of instructions
  Two instructions
Limitations
  Early: instructions placement and types
    Example: integer instruction must be first
  Modern superscalars dropped this restriction

## Slide 13: Three Steps Involved in Fetch And Issue
1. Fetch two instructions from the cache
2. Determine 0, 1 or 2 instructions can issue
3. Issue them to the correct FUs
  More ports for FP registers to do FP load & FP op in a pair

## Slide 14: Superscalar MIPS in Operation
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Integer | IF | ID | EX | MEM | WB |  |  | 
FP | IF | ID | EX | EX | EX | WB |  | 
Integer |  | IF | ID | EX | MEM | WB |  | 
FP |  | IF | ID | EX | EX | EX | WB | 
Integer |  |  | IF | ID | EX | MEM | WB | 
FP |  |  | IF | ID | EX | EX | EX | WB
Integer |  |  |  | IF | ID | EX | MEM | WB
FP |  |  |  | IF | ID | EX | EX | EX

## Slide 15: Long FP Operations
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Integer | IF | ID | EX | MEM | WB |  |  | 
FP | IF | ID | EX | EX | EX | WB |  | 
Integer |  | IF | ID | EX | MEM | WB |  | 
FP |  | IF | ID | EX | EX | EX | WB | 
Integer |  |  | IF | ID | EX | MEM | WB | 
FP |  |  | IF | ID | EX | EX | EX | WB
Integer |  |  |  | IF | ID | EX | MEM | WB
FP |  |  |  | IF | ID | EX | EX | EX

## Slide 16: Problems
A large set of bypass will be needed
The FP datapath bottleneck
  Pipelined/Multiple FP units
  1 cycle load delay expands to 3 instructions
    An instruction in another FP half can’t use it
    Nor instructions in next slot
More ambitious compiler or hardware scheduling techniques
  Otherwise a superscalar processor is likely to provide little or no additional performance

## Slide 17: Tomasulo's Algorithm with Multiple Issue
Extend Tomasulo’s algorithm
Assume
  Do not issue instructions out-of-order
  Separate the data structures for the integer and floating-point registers (how to?)
  Simultaneously issue a floating-point instruction and an integer instruction to their respective reservation stations
    As long as they do not access the same register set

## Slide 18: Two Approaches of Multiple Issue
Pipelined
  Run this step in half a clock cycle
  Two instructions can be issued in one clock cycle
Widen the issue logic
  Build the logic necessary to handle two instructions at once
Modern real superscalar processors
  Issue 4 or more instructions per clock often include both approaches
  They both pipeline and widen the issue logic

## Slide 19: A MIPS & Tomasulo’s Example
Loop: L.D F0,0(R1)
ADD.D F4,F0,F2
S.D F4,0(R1)
DADDIU R1,R1,#-8
BNE R1,R2,Loop

## Slide 20: Assume 1
Both a FP and an INT operation can be issued on every clock cycle
  One INT functional unit used for both ALU operations and effective address calculations
  A separate pipelined FP functional unit
The number of cycles of latency
  1 cycle for integer ALU operations
  2 cycles for loads
  3 cycles for FP add

## Slide 21: Assume 2
Two CDBs
About branch instruction
  Branches single issue
  No delayed branches (no delay slot)
  There is dynamic branch-prediction hardware and a separate functional unit to evaluate branch conditions
    There is a branch unit
  Branch prediction is perfect

## Slide 22: Work Is: Create a Table Showing
When each instruction issues, execution, and writes its result to the CDB for the first three iterations of the loop
The resource usage for
  The integer unit
  The floating point unit
  The data cache
  The CDB

## Slide 23: A Dual-issue Version of Our Tomasulo Pipeline 1
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 |  |  |  | First issue
1 | ADD.D F4,F0,F2 |  |  |  |  | 
1 | S.D F4,0(R1) |  |  |  |  | 
1 | DADDIU R1,R1,#-8 |  |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 24: A Dual-issue Version of Our Tomasulo Pipeline 2
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 |  |  |  |  | 
1 | S.D F4,0(R1) |  |  |  |  | 
1 | DADDIU R1,R1,#-8 |  |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 25: A Dual-issue Version of Our Tomasulo Pipeline 3
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 |  |  |  | 
1 | S.D F4,0(R1) |  |  |  |  | 
1 | DADDIU R1,R1,#-8 |  |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 26: A Dual-issue Version of Our Tomasulo Pipeline 4
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  |  | Wait for L.D
1 | S.D F4,0(R1) |  |  |  |  | 
1 | DADDIU R1,R1,#-8 |  |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 27: A Dual-issue Version of Our Tomasulo Pipeline 5
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | 3 cycles letncy for ADD.D
1 | S.D F4,0(R1) |  |  |  |  | 
1 | DADDIU R1,R1,#-8 |  |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 28: A Dual-issue Version of Our Tomasulo Pipeline 6
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 |  |  |  | 
1 | DADDIU R1,R1,#-8 | 2 |  |  |  | 
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 29: A Dual-issue Version of Our Tomasulo Pipeline 7
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 |  |  | 
1 | DADDIU R1,R1,#-8 | 2 | 4 |  |  | Wait for ALU
1 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 30: A Dual-issue Version of Our Tomasulo Pipeline 8
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | 1 cycle
1 | BNE R1,R2,Loop | 3 |  |  |  | 

## Slide 31: A Dual-issue Version of Our Tomasulo Pipeline 9
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU

## Slide 32: A Dual-issue Version of Our Tomasulo Pipeline 10
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) |  |  |  |  | 
2 | ADD.D F4,F0,F2 |  |  |  |  | 
2 | S.D F4,0(R1) |  |  |  |  | 
2 | DADDIU R1,R1,#-8 |  |  |  |  | 
2 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 33: A Dual-issue Version of Our Tomasulo Pipeline 11
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 |  |  |  | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 |  |  |  | 
2 | S.D F4,0(R1) |  |  |  |  | 
2 | DADDIU R1,R1,#-8 |  |  |  |  | 
2 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 34: A Dual-issue Version of Our Tomasulo Pipeline 12
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 |  |  |  | 
2 | S.D F4,0(R1) |  |  |  |  | 
2 | DADDIU R1,R1,#-8 |  |  |  |  | 
2 | BNE R1,R2,Loop |  |  |  |  | 

## Slide 35: A Dual-issue Version of Our Tomasulo Pipeline 13
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for L.D
2 | S.D F4,0(R1) | 5 |  |  |  | 
2 | DADDIU R1,R1,#-8 | 5 |  |  |  | 
2 | BNE R1,R2,Loop | 6 |  |  |  | 

## Slide 36: A Dual-issue Version of Our Tomasulo Pipeline 14
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for L.D
2 | S.D F4,0(R1) | 5 | 8 |  |  | Wait for ALU for A
2 | DADDIU R1,R1,#-8 | 5 |  |  |  | 
2 | BNE R1,R2,Loop | 6 |  |  |  | 

## Slide 37: A Dual-issue Version of Our Tomasulo Pipeline 15
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for L.D
2 | S.D F4,0(R1) | 5 | 8 | 14 |  | Wait for ADD.D
2 | DADDIU R1,R1,#-8 | 5 |  |  |  | 
2 | BNE R1,R2,Loop | 6 |  |  |  | 

## Slide 38: A Dual-issue Version of Our Tomasulo Pipeline 16
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for L.D
2 | S.D F4,0(R1) | 5 | 8 | 14 |  | Wait for ADD.D
2 | DADDIU R1,R1,#-8 | 5 | 9 |  | 10 | Wait for ALU
2 | BNE R1,R2,Loop | 6 | 11 |  |  | Wait for DADDIU

## Slide 39: A Dual-issue Version of Our Tomasulo Pipeline 17
Iter. # | Instructions | Issues | Exec. | Mem. access | Write CDB | Comment
1 | L.D F0,0(R1) | 1 | 2 | 3 | 4 | First issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for L.D
1 | S.D F4,0(R1) | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,#-8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DADDIU
2 | L.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for L.D
2 | S.D F4,0(R1) | 5 | 8 | 14 |  | Wait for ADD.D
2 | DADDIU R1,R1,#-8 | 5 | 9 |  | 10 | Wait for ALU
2 | BNE R1,R2,Loop | 6 | 11 |  |  | Wait for DADDIU
3 | L.D F0,0(R1) | 7 | 12 | 13 | 14 | Wait for BNE
3 | ADD.D F4,F0,F2 | 7 | 15 |  | 18 | Wait for L.D
3 | S.D F4,0(R1) | 8 | 13 | 19 |  | Wait for ADD.D
3 | DADDIU R1,R1,#-8 | 8 | 14 |  | 15 | Wait for ALU
3 | BNE R1,R2,Loop | 9 | 16 |  |  | Wait for DADDIU

## Slide 40: Resource Usage Table
Clock | Integer ALU | FP ALU | Data Cache | CDB
1 |  |  |  | 
2 | 1/ L.D |  |  | 
3 | 1 / S.D |  | 1/ L.D | 
4 | 1 / DADDIU |  |  | 1/ L.D
5 |  | 1 / ADD.D |  | 1 / DADDIU
6 |  |  |  | 
7 | 2 / L.D |  |  | 
8 | 2 / S.D |  | 2 / L.D | 1 / ADD.D
9 | 2 / DADDIU |  | 1 / S.D | 2 / L.D
10 |  | 2 / ADD.D |  | 2 / DADDIU
11 |  |  |  | 
12 | 3 / L.D |  |  | 
13 | 3 / S.D |  | 3 / L.D | 2 / ADD.D
14 | 3 / DADDIU |  | 2 / S.D | 3 / L.D
15 |  | 3 / ADD.D |  | 3 / DADDIU
16 |  |  |  | 
17 |  |  |  | 
18 |  |  |  | 3 / ADD.D
19 |  |  | 3 / S.D | 

## Slide 41: Answer
The loop will continue to fetch and issue a new loop iteration every three clock cycles
Sustaining one iteration in three cycles
  IPC of 5/3 = 1.67
The instruction execution rate is lower
  Instruction completion rate 15/16 = 0.94
The issue unit will eventually fill all the reservation stations and will stall

## Slide 42: Superscalar Machines: Problems
Issuing two instructions will require fetching (IF) and decoding (ID) two instructions (64 bits)
  Assume: instructions are paired and aligned and on 64-bit boundaries
  The integer portion appearing first
  Issue one of each type per cycle
A branch delay in our example can also affect the next three instructions

## Slide 43: Control Complexity: MIPS R10000
Control Logic
[ SGI/MIPS Technologies Inc., 1995 ]

## Slide 44: The VLIW
3.7 Multiple Issue

## Slide 45: The VLIW
A LIW (Long Instruction Word) or a VLIW (Very Long instruction Word) architecture
The first commercial LIW processor was the AP-120B developed by Floating Point Systems
A later model, the FPS-164, had 10 instructions per wide word for 10 separate functional units

## Slide 46: Rely on VLIW Compiler Technology
To minimize the potential data hazard stalls
To actually format the instructions in a potential issue packet
  It issue a package of instructions within the fields rather than trying to issue multiple independent instructions to the units

## Slide 47: The VLIW Compiler Must…
The VLIW hardware need not check explicitly for dependences
To ensure that dependences within the issue packet cannot be present or
At a minimum, indicate when a dependence may be present

## Slide 48: The Potential Advantages of VLIW
Simpler hardware
Still exhibiting good performance through extensive compiler optimization
The VLIW organization
  Uses multiple independent units
  Packages the multiple operations into one long instruction word

## Slide 49: The VLIW Instructions
A VLIW instruction would have a set of fields for each functional unit
  Perhaps 16 to 24 bits per unit
It might include following seven units
  Two integers
  Two floating-points
  Two memory references
  A branch
An instruction length from 112 to 168 bits

## Slide 50: Early VLIWs: Quite Rigid
The hardware simply sends the appropriate fields to the FUs
The compiler is responsible for
  Keeping each FU is busy for each cycle
  Putting in a NOP for any unit that has no work to do
Effectively required re-compile of programs for different versions of the hardware

## Slide 51: Recent Architectures
Still requiring the compiler to do most of the work of finding and scheduling instructions for parallel execution
Being pursued for desktop and server markets
  Transmeta (bankrupt) Crusoe (The hero of the England writer Defoe’s Robinson Crusoe)
  Intel Itanium

## Slide 52: A VLIW Example
Scheduling the loop for a VLIW machine with
  Two memory references
  Two FP operations
  One integer/branch operation
Gives us the following code sequence:
  Loop x[i] = x[i] + s

## Slide 53: The VLIW Example Code
  Loop: L.D F0,0(R1)
  ADD.D F4,F0,F2
  S.D F4,0(R1)
  DADDUI R1,R1,#-8
  BNE R1,R2,Loop
The loop has been unrolled to make seven copies of the body

## Slide 54: The VLIW Example Execution
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) | L.D F14,-24(R1) |  |  | 
L.D F18,-32(R1) | L.D F22,-40(R1) | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
L.D F26,-48(R1) |  | ADD.D F12,F10,F2 | ADD.D F16,F14,F2 | 
 |  | ADD.D F20,F18,F2 | ADD.D F24,F22,F2 | 
S.D F4,0(R1) | S.D F8,-8(R1) | ADD.D F28,F26,F2 |  | 
S.D F12,-16(R1) | S.D F16,-24(R1) |  |  | DADDUI R1,R1,#-56
S.D F20,24(R1) | S.D F24,16(R1) |  |  | 
S.D F28,8(R1) |  |  |  | BNE R1,R2,Loop
7 results in 9 cycles, or 1.29 cycles per result
The issue rate is 23 operations in 9 clock cycles
  2.5 operations/cycle

## Slide 55: The VLIW Example Performance
1.29 cycles per result
  Nearly twice as fast as the two-issue static superscalar (2.4 clock cycles per element, see F4.2/p313)
2.5 operations per cycle
  The efficiency, the used slots, is about 51% (23/45)

## Slide 56: The Registers in VLIW Example
It requires a larger number of registers than MIPS would normally use
  2*7+1=15 FP regs
The base MIPS use only 3 (2*1+1) FP registers
  See the code in p305
In the superscalar example 11 (2*5+1) registers were needed

## Slide 57: The VLIW without Empty Issue
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) |  |  |  | 
 |  | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
 |  | ADD.D F12,F10,F2 |  | 
 |  |  |  | DADDUI R1,R1,#-24
S.D F4,24(R1) | S.D F8,16(R1) |  |  | 
S.D F12,8(R1) |  |  |  | 
 |  |  |  | BNE R1,R2,Loop
3 results in 8 cycles, or 2.66 cycles per result
Efficiency of operation slot: 11/40 = 27.5%

## Slide 58: The VLIW without Empty FP-op
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) | L.D F14,-24(R1) |  |  | 
L.D F18,-32(R1) | L.D F22,-40(R1) | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
L.D F26,-48(R1) | L.D F30,-56(R1) | ADD.D F12,F10,F2 | ADD.D F16,F14,F2 | 
L.D F34,-64(R1) | L.D F38,-72(R1) | ADD.D F20,F18,F2 | ADD.D F24,F22,F2 | DADDUI R1,R1,#-80
S.D F4,80(R1) | S.D F8,72(R1) | ADD.D F28,F26,F2 | ADD.D F32,F30,F2 | 
S.D F12,64(R1) | S.D F16,56(R1) | ADD.D F36,F34,F2 | ADD.D F40,F38,F2 | 
S.D F20,48(R1) | S.D F20,40(R1) |  |  | 
S.D F20,32(R1) | S.D F20,24(R1) |  |  | 
S.D F20,16(R1) | S.D F20,8(R1) |  |  | BNE R1,R2,Loop
10 results in 10 cycles with 42 FP registers (if available), or 1.00 cycles per result
Efficiency of operation slot: 36/50 =72%

## Slide 59: Problems Of VLIW
The technical problems
  The increase in code size
  And the limitations of lock-step operation
A major logistical problem
  Binary code compatibility

## Slide 60: Two Reasons to Increase Code Size
A vast amount of independent operations
  Generating operations in a straight-line code fragment requires ambitiously unrolling loops
  >Exploiting large amounts of ILP
Low efficiency usage of FUs
  The unused functional units translate to wasted bits in the instruction encoding
  In previous example, about 51% of the functional units were used

## Slide 61: Decrease VLIW Code Size
Set one large immediate field for use by any functional unit
Compress the instructions in main memory and expand them when they are read into the cache or are decoded
  By hardware

## Slide 62: VLIW’s Lock-step Operation
Lock-step: all the FUs must synchronize
There was no hazard detection hardware
A stall in any FU must cause the entire processor to stall

## Slide 63: Long Lock-step: Memory Reference
Predicting which data will encounter a cache stall and scheduling them is very difficult
As the issue rate and number of memory references becomes large, this synchronization restriction becomes unacceptable

## Slide 64: VLIW’s Lock-step Under H/W
In more recent processors, the functional units operate more independently
The compiler is used to avoid hazards at issue time
Hardware checks allow for unsynchronized execution once instructions are issued
  Dynamic VLIW approach

## Slide 65: Binary Code Compatibility
A VLIW code sequence is decided by
  The instruction set
  The detailed pipeline structure
  FUs and their latencies
Different numbers of FUs and unit latencies require different versions of the code
  The ability to run old binary files is an advantage of the superscalar

## Slide 66: Solution to Code Migration
Object-code translation or emulation
  This technology is developing quickly and could play a significant role in future migration schemes
Temper the strictness
  So that binary compatibility is still feasible
  This approach is used in the IA-64

## Slide 67: The Future of VLIW
Some vendors are betting VLIW is the future
  Intel/HP has stated that they will use VLIW-like for Merced core instead of the RISC core of the Pentium Pro, the Pentium II, III, and 4
  Transmeta is using VLIW in the Crusoe microprocessors
Many now architectures use the features of VLIW, or use VLIW in calculate unit

## Slide 68: Next ...
Branch Target Buffer and
The Limitations of ILP