## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 09 BTB & ILP Limitation
December 9, 2020

## Slide 4: My View: Enthusiasm of Students
Chart: Enthusiasm
| Vacation | The first lesson | 0.5 hour after | A week before exam | Last day | last night | Durning | After exam | Anouncement
Enthusiasm | 1 | 1.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.3 | 0.9 | 1.3 | 1 | 0.1

## Slide 5: Superscalar – Hi Story
IBM pioneering work: John Cocke
  ACS, A eventually canceled 1960’s project: follow Stretch (the first general-purpose pipelined processor, the IBM 7030) and surpass the CDC 6600/6800
  An mid-1980s research processor: “America”, coined the term superscalar
  The 1989 Power-1 of RS/6000 was the first to use this approach
Today practically all RISC like processors use superscalar
  Issue a small number (1~8) of instructions per cycle

## Slide 6: MIPS Branches and Jumps
Each instruction fetch depends on one or two pieces of information from the preceding instruction:
  1) Is the preceding instruction a taken branch?
  2) If so, what is the target address?
Instruction | Taken known? | Target known?
J | After Inst. Decode | After Inst. Decode
JR | After Inst. Decode | After Reg. Fetch
BEQZ/BNEZ | After Reg. Fetch* | After Inst. Decode
*Assuming zero detect on register read |  | 

## Slide 7: Control Flow Penalty
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution!
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch

## Slide 8: Control Flow Penalty
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution!
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started

## Slide 9: Control Flow Penalty
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
  ~ Loop length x pipeline width
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started

## Slide 10: Branch Penalties in Modern Pipelines
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)
Branch Target Address Known
Branch Direction &
Jump Register Target Known
UltraSPARC-III instruction fetch pipeline stages
(in-order issue, 4-way superscalar, 750MHz, 2000)

## Slide 11: Multiple Issue Processors
Delivering 4~8 instructions per cycle
  Predicting branches well is not enough
  Must deliver a high band-width instruction stream
Three concepts to accomplish
  A branch target buffer
  An integrated instruction fetch unit
  Predicting return addresses
We Need
  High performance instruction delivery

## Slide 12: Branch Target Buffer (BTB)
Find the target PC before ID
  Just like a ordinary instruction fetch after a branch
Fields of a BTB
  The PC of a branch stores in BTB
  The predicted PC (target address) stores in BTB
  (An optional field to indicate if the branch is predicted to be taken or not taken)
Also called branch-target cache

## Slide 13: How Branch Target Buffer Works
IF: The PC of every instruction is compared against the PC’s in the BTB buffer
If matched meaning the instruction is a branch, the corresponding predicted PC is returned
(If the branch was predicted taken,) the predicted PC is used as the next PC

## Slide 14: Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only predicted taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB (can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 16: BTB Penalties
Instruction in BTB | Prediction | Actual branch | Penalty cycle
yes | T | T | 0
yes | T | NT | 2
no |  | T | 2
no |  | NT | 0

## Slide 17: One Variation of BTB
One or more instructions instead of, or in addition to, the predicted target address
  One target buffer or
  Two legs
Minimized the times of instruction fetch from memory
  Allows a larger BTB

## Slide 18: BTB : Structure

## Slide 19: BTB : Usage
If a branch is detected and the predicted PC is correct we have a zero-delay or a zero-cycle branch
  The IBM RS/6000 and several PowerPC uses this technique of branch prediction
  Intel Pentium…

## Slide 20: BTB Reduced the Penalty
Fetching instruction from both direction
Adds cost
  Need dual ported memory system
  It may be the only way to reduce branch penalties
The PowerPC processors in IBM AS/400
  Fetching both branch legs

## Slide 21: BTB : Example
Consider the example in BPB
  Taken 9 and not taken once
Assuming the penalty as the table
Determine the total branch penalty

## Slide 22: BTB : Example Assumptions
Prediction accuracy: 90%
  For instruction in buffer
Hit rate in the buffer: 90%
  For branches predicted taken

## Slide 23: BTB : Answer 1/2
Probability (branch in buffer, but not taken)
=Percent buffer hit rate × Percent incorrect predictions
=90% × 10%
=0.09

## Slide 24: BTB : Answer 2/2
Probability (branch not in buffer, but actually taken) = 10%
Branch penalty = (0.09 + 0.10) × 2 = 0.38

## Slide 25: One Variation of BTB
One or more instructions instead of, or in addition to, the predicted target address
  One target buffer or
  Two legs
Minimized the times of instruction fetch from memory
  Allows a larger BTB

## Slide 26: Branch Folder
Branch folding: buffering the actual target instructions to perform an optimization
Branch folder buffers the instructions from the predicated path obtain
  Zero-cycle unconditional branch
  Zero-cycle conditional branch

## Slide 27: Indirect Jumps 1/2
Including in most recent processors, generated in high-level language
  SELECT or CASE statement
  GOTO statement in FORTAIN-like language
  Indirect procedure CALL
  Procedure RETURN: 85% of indirect jump in SPEC

## Slide 28: Indirect Jumps 2/2
A small buffer of return addresses is used to overcome this problem
  Operating as stack has been proposed
  Cache the most recent return address
Depth
  Cost

## Slide 29: Prediction Accuracy (Depth)

## Slide 30: Dynamic Branch Prediction Summary
BPB/BHT: 2 bits for loop accuracy
  Correlation: recently executed branches correlated with next branch
    Either different branches or different executions of same branches
Branch Target Buffer
  Include branch address & prediction

## Slide 31: BTB vs. BPB
BPB are limited by
  Prediction accuracy
  The penalty for the missed predictions
BTB accuracy range depending on
  The program
  Size of the buffer
Typical BTB achieve an 80~95%

## Slide 32: Conclusion of Branch Prediction
Prediction accuracy: typical 80 - 90%, depending on
  Type of program
  Size of buffer
Penalty for misprediction
  Fetch both direction: dual-port memory, interleaved cache
  Cache multiple paths in the target buffer

## Slide 33: Question: Where Can Implement These Functions?
Almost all branch predictions associate with instruction flow
  The NPC and its calculation or decision
  Fetch or prefetch which instructions
So, the answer is
  it must be instruction fetch unit (IFU)

## Slide 34: Integrated Instruction Fetch Units
To meet the demands of multiple issue
As a separate autonomous unit that feeds instructions to the rest of the pipeline
Characterizing instruction fetch as a simple single pipe stage
  The complexities of multiple issue is no longer valid

## Slide 35: Integrates Functions
Integrated branch prediction
  Becomes part of the instruction fetch unit
  Constantly predicting branches
  Drive the fetch pipeline
Instruction prefetch
  Deliver multiple instructions per clock
  Fetch ahead
  Manages the instruction prefetching
Instruction Memory Access

## Slide 36: Next …
Studies of the Limitations of ILP

## Slide 37: Critical Question
How much ILP exists
  Long-term ability to enhance performance at rate that exceeds the increase in speed of the base IC technology
What is need to exploit more ILP
  Both for computer and compiler design
How much ILP is available using existing mechanisms with increasing hardware budgets?

## Slide 38: New ILP Techniques ???
Need to invent new HW/SW mechanisms to keep on processor performance curve?
E.g.
  Intel MMX, SSEx, AVX (Streaming SIMD Extensions):
    64 bits in ints
    128 bits in floats, including 2 64-bit FPs
  Power/PowerPC
  Sparc
  Streaming – DSP applications

## Slide 39: How to Study ILP?
Making a set of assumptions
How much parallelism is available under these assumptions
  Making the fewest assumptions
  It is completely unrealizable in ultimate hardware
The affection on the compiler and hardware design

## Slide 40: HW Model: An Ideal Processor
1. Infinite number of virtual register
  Unlimited register renaming
  No name (WAW and WAR) hazards
2. Perfect branch prediction
  All conditional branch are predicted exactly
3. Perfect jump prediction
  Perfect speculation and unbounded ROB
4. Perfect alias analysis
5. Perfect cache
  All memory accesses take 1 clock cycle

## Slide 41: These Assumptions Means
Eliminate all name dependences
  Assumptions 1 (registers) and 4 (memory)
Eliminate all control dependences
  Assumptions 2 and 3
Any instruction can immediately execute just following which it depends on
  Real dependences are ideally processed
A processor that can issue an unlimited number of instructions at once looking arbitrarily far ahead in the computation

## Slide 42: Perfect Processor HW Model
Functions | Model | Power 8 (2014)
Instructions Issued per clock | Infinite | 10
Execution units | Infinite | 16
Instruction Window Size | Infinite | Hundreds
Renaming Registers | Infinite | 48 integer+40 Fl. Pt. (?)
Branch Prediction | Perfect | 2% to 6% misprediction
Cache | Perfect | 64KD, 32KI, 512KB L2, 8MB L3 (one core)
Memory Alias Analysis | Perfect | ??

## Slide 43: What the Perfect Processor Must Do?
Look arbitrarily far ahead to find a set of instructions to issue
Determine all register dependences
Determine all memory dependences
Avoid all registers WAW and WAR hazards
Predict all branches
Enough FUs for ready instructions to issue

## Slide 44: ILP in a Perfect Processor (SPEC92)
Chart: 
| gcc | expresso | li | fpppp | doduc | tomcatv
ILP | 54.8 | 62.6 | 17.9 | 75.2 | 118.7 | 150.1
instructions issued per cycle

## Slide 45: The Factors We are Concerned
The instruction windows
Branch prediction
The effects of register number
Alias analysis
Ways(number) of instruction issue

## Slide 46: Instruction Windows
The set of instructions examined for simultaneous execution
  Limits the max number of instructions for issue
Window size: hundreds, 2010
  About 2450 comparisons for size 50 (900 for 30)
  IBM Power5: over 200 instructions in flight
    Issue 4 inst./clk to 6 executions
    88 integer and 88 floating points registers for renaming

## Slide 47: Complexity of Instruction Windows
To determine n issuing register-register dependences, requires comparisons
  2(n-1) comparisons for the 1st instruction
  2(n-2) for the 2nd
  …
  Total is
    2(n-1) + 2(n-2) + … + 2 = n(n-1) = n^2 + n
    4 million for 2000 instructions
Recent machine: several windows
  2~8 windows

## Slide 48: Limits to ILP HW Model
Functions | Real Model | Ideal Model
Instructions issued per clock | Infinite | Infinite
Instruction window size | Infinite, 2K, 512, 128, 32 | Infinite
Renaming registers | Infinite | Infinite
Branch prediction | Perfect | Perfect
Cache | Perfect | Perfect
Memory alias | Perfect | Perfect

## Slide 49: Limitation of the Window Size
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Infinite | 55 | 63 | 18 | 75 | 119 | 150
2K | 36 | 41 | 15 | 61 | 59 | 60
512 | 10 | 15 | 12 | 49 | 16 | 45
128 | 10 | 13 | 11 | 35 | 15 | 34
32 | 8 | 8 | 9 | 14 | 9 | 14
instructions issued per cycle

## Slide 50: Limitation of the Window Size
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Infinite | 55 | 63 | 18 | 75 | 119 | 150
2K | 36 | 41 | 15 | 61 | 59 | 60
512 | 10 | 15 | 12 | 49 | 16 | 45
128 | 10 | 13 | 11 | 35 | 15 | 34
32 | 8 | 8 | 9 | 14 | 9 | 14
instructions issued per cycle

## Slide 51: Limitation of the Window Size
Chart: 
| Infinite | 2K | 512 | 128 | 32
gcc | 55 | 36 | 10 | 10 | 8
espresso | 63 | 41 | 15 | 13 | 8
li | 18 | 15 | 12 | 11 | 9
fpppp | 75 | 61 | 49 | 35 | 14
doduc | 119 | 59 | 16 | 15 | 9
tomcatv | 150 | 60 | 45 | 34 | 14
instructions issued per cycle
The amount of parallelism uncovered falls sharply with decreasing instruction windows size

## Slide 52: Branch and Jump Prediction 1/2
Perfect
  Perfectly predicted at the start of execution
Tournament-based branch predictor
  2^13 (8K) entries, three 2-bit fields
  correlating 2-bit predictor, with global history
  noncorrelating 2-bit predictor
  2-bit selector: correlating/noncorrelating

## Slide 53: Branch and Jump Prediction 2/2
Standard 2-bit with 512 entries BPB
  16 entries to predict returns, in addition
Static
  Using profile history of the program by compiler
None
  Jumps are still predicted

## Slide 54: Limits to ILP HW Model
Functions | New Model | Model
Instructions issued per clock | 64 | Infinite
Instruction window size | 2048 | Infinite
Renaming registers | Infinite | Infinite
Branch prediction | Perfect vs. 8K Tournament vs. 512 2-bit vs. profile vs. None | Perfect
Cache | Perfect | Perfect
Memory alias | Perfect | Perfect

## Slide 55: Branch and Jump Prediction
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Perfect | 35 | 41 | 16 | 61 | 15 | 60
Tournament predictor | 9 | 12 | 10 | 48 | 13 | 46
2-bit | 6 | 7 | 6 | 46 | 14 | 45
Static | 6 | 6 | 7 | 45 | 4 | 45
None | 2 | 2 | 2 | 29 | 4 | 6
instructions issued per cycle

## Slide 56: Branch and Jump Prediction
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Perfect | 35 | 41 | 16 | 61 | 15 | 60
Tournament predictor | 9 | 12 | 10 | 48 | 13 | 46
2-bit | 6 | 7 | 6 | 46 | 14 | 45
Static | 6 | 6 | 7 | 45 | 4 | 45
None | 2 | 2 | 2 | 29 | 4 | 6
instructions issued per cycle

## Slide 57: IIPC: Branch and Jump Prediction
Chart: 
| Perfect | Tournament predictor | 2-bit | Static | None
gcc | 35 | 9 | 6 | 6 | 2
espresso | 41 | 12 | 7 | 6 | 2
li | 16 | 10 | 6 | 7 | 2
fpppp | 61 | 48 | 46 | 45 | 29
doduc | 15 | 13 | 14 | 4 | 4
tomcatv | 60 | 46 | 45 | 45 | 6
No much difference
instructions issued per cycle

## Slide 58: Branch Prediction Accuracy
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Perfect | 0.88 | 0.86 | 0.88 | 0.86 | 0.95 | 0.99
2-bit | 0.7 | 0.82 | 0.77 | 0.82 | 0.84 | 0.99
Tournament predictor | 0.94 | 0.96 | 0.98 | 0.98 | 0.97 | 1

## Slide 59: Branch Misprediction Rates
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
perfrct | 0.12 | 0.14 | 0.12 | 0.14 | 0.05 | 0.01
2-bit | 0.3 | 0.18 | 0.13 | 0.18 | 0.16 | 0.01
Tournament predictor | 0.06 | 0.04 | 0.02 | 0.02 | 0.03 | 0

## Slide 60: Misprediction Rates
Chart: 
| Profile-based | 2-bit counter | Tournament
tomcatv | 0.01 | 0.01 | 0
doduc | 0.05 | 0.16 | 0.03
fpppp | 0.14 | 0.18 | 0.02
li | 0.12 | 0.23 | 0.02
espresso | 0.14 | 0.18 | 0.04
gcc | 0.12 | 0.3 | 0.06

## Slide 61: The Effects of Register Number
Ideal processor
  Using an infinite set of physical registers
  Eliminates all name dependences among register references
Alpha 21264 registers:
  32 integer and 32 FP architectural registers
  41 integer and 41 FP extended registers
The effect of reducing the number of registers available for renaming
  Both the FP and GP registers are increased

## Slide 62: Limits to ILP HW Model
Functions | New Model | Model
Instructions issued per clock | 64 | Infinite
Instruction window size | 2048 | Infinite
Renaming registers | Infinite v. 256, 128, 64, 32, none | Infinite
Branch prediction | 8K 2-bit | Perfect
Cache | Perfect | Perfect
Memory alias | Perfect | Perfect

## Slide 63: The Effects of Register Number
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
infinite | 11 | 15 | 12 | 59 | 29 | 54
256 | 10 | 15 | 12 | 49 | 16 | 45
128 | 10 | 13 | 12 | 35 | 15 | 44
64 | 9 | 10 | 11 | 20 | 11 | 28
32 | 5 | 5 | 6 | 5 | 5 | 7
none | 4 | 4 | 5 | 4 | 5 | 5
Instruction issues per cycle

## Slide 64: The Effects of Register Number
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
infinite | 11 | 15 | 12 | 59 | 29 | 54
256 | 10 | 15 | 12 | 49 | 16 | 45
128 | 10 | 13 | 12 | 35 | 15 | 44
64 | 9 | 10 | 11 | 20 | 11 | 28
32 | 5 | 5 | 6 | 5 | 5 | 7
none | 4 | 4 | 5 | 4 | 5 | 5
Instruction issues per cycle

## Slide 65: The Effects of Register Number
Chart: 
| infinite | 256 | 128 | 64 | 32 | none
gcc | 11 | 10 | 10 | 9 | 5 | 4
espresso | 15 | 15 | 13 | 10 | 5 | 4
li | 12 | 12 | 12 | 11 | 6 | 5
fpppp | 59 | 49 | 35 | 20 | 5 | 4
doduc | 29 | 16 | 15 | 11 | 5 | 5
tomcatv | 54 | 45 | 44 | 28 | 7 | 5
Instruction issues per cycle

## Slide 66: Alias Analysis
Global/stack perfect
  Perfect prediction for global and stack
  All heap reference are conflict
Inspection
  Static determination
None
  All memory reference are assumed to conflict

## Slide 67: Limits to ILP HW Model
Functions | New Model | Model
Instructions issued per clock | 64 | Infinite
Instruction window size | 2048 | Infinite
Renaming registers | 256 Int + 256 FP | Infinite
Branch prediction | 8K 2-bit | Perfect
Cache | Perfect | Perfect
Memory alias | Perfect v. Stack v. Inspect v. none | Perfect

## Slide 68: Effect of Alias Analysis
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Perfect | 10 | 15 | 12 | 49 | 16 | 45
Global/stack | 7 | 7 | 9 | 49 | 16 | 45
Inspection | 4 | 5 | 4 | 4 | 6 | 5
None | 3 | 5 | 3 | 3 | 4 | 4
Instruction issues per cycle

## Slide 69: Effect of Alias Analysis
Chart: 
| gcc | espresso | li | fpppp | doduc | tomcatv
Perfect | 10 | 15 | 12 | 49 | 16 | 45
Global/stack | 7 | 7 | 9 | 49 | 16 | 45
Inspection | 4 | 5 | 4 | 4 | 6 | 5
None | 3 | 5 | 3 | 3 | 4 | 4
Instruction issues per cycle

## Slide 70: Effect of Alias Analysis
Chart: 
| Perfect | Global/stack | Inspection | None
gcc | 10 | 7 | 4 | 3
espresso | 15 | 7 | 5 | 5
li | 12 | 9 | 4 | 3
fpppp | 49 | 49 | 4 | 3
doduc | 16 | 16 | 6 | 4
tomcatv | 45 | 45 | 5 | 4
Instruction issues per cycle

## Slide 71: Dynamic Memory Disambiguation
We must know the memory addresses of all earlier stores that not yet committed
Only a small number of memory references can be disambiguated per clock cycle
The size of the load/store buffers
  They determines how much load or store may be moved

## Slide 72: Memory Address Speculation
One technique for reducing this limitation on in-order address calculation
No memory dependences exist or uses a hardware to predict if a dependence exists, stalling the load if a dependence is predicted
A mechanism to discover if a dependence truly exists and to recover if so

## Slide 73: Realizable Processors Assumptions
Up to 64 instruction issues per clock with no issue restrictions
A tournament predictor with 1K entries and a 16-entry return predictor
Perfect disambiguation of memory references done dynamically
Register renaming with 64 additional integer and 64 additional FP registers

## Slide 74: Limits to ILP HW Model
Functions | New Model | Model
Instructions issued per clock | 64 (no restrictions) | Infinite
Instruction window size | Infinite vs. 256, 128, 64, 32 | Infinite
Renaming registers | 64 Int + 64 FP | Infinite
Branch prediction | 1K 2-bit + 16 return | Perfect
Cache | Perfect | Perfect
Memory alias | HW disambiguation | Perfect

## Slide 75: Parallelism and Window Size
Chart: Instruction issues per cycle
| Infinite | 256 | 128 | 64 | 32 | 16 | 8 | 4
gcc | 10 | 10 | 10 | 9 | 8 | 6 | 4 | 3
espresso | 15 | 15 | 13 | 10 | 8 | 6 | 4 | 2
li | 12 | 12 | 11 | 11 | 9 | 6 | 4 | 3
fpppp | 52 | 47 | 35 | 22 | 14 | 8 | 5 | 3
doduc | 17 | 16 | 15 | 12 | 9 | 7 | 4 | 3
tomcatv | 56 | 45 | 34 | 22 | 14 | 9 | 6 | 3

## Slide 76: Parallelism and Window Size
Chart: Instruction issues per cycle
| gcc | espresso | li | fpppp | doduc | tomcatv
Infinite | 10 | 15 | 12 | 52 | 17 | 56
256 | 10 | 15 | 12 | 47 | 16 | 45
128 | 10 | 13 | 11 | 35 | 15 | 34
64 | 9 | 10 | 11 | 22 | 12 | 22
32 | 8 | 8 | 9 | 14 | 9 | 14
16 | 6 | 6 | 6 | 8 | 7 | 9
8 | 4 | 4 | 4 | 5 | 4 | 6
4 | 3 | 2 | 3 | 3 | 3 | 3

## Slide 77: Homeworks
Review
  3.9
  3.10 (the 5th ed)
Reading
  "Combining Branch Predictors", McFarling, DEC WRL Technical Note TN-36, 1993
Coding
  The branch predictor: BPB(1k, 2bit) + BTB(256, …)

## Slide 78: Next
MT & DLP