## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 10 Processor Examples

## Slide 3: 学术不端行为三宗罪（FFP）
一、伪造（Fabrication）：编造研究记录或结果
  无中生有地捏造
二、虚假（Falsification）：对材料、设备、过程、结果等进行作假，包括故意地筛选、篡改研究记录等
  有点影子，确实做过，但得不到想要的结果，就往自己希望看到的方向修改结果
  用PS加工试验图表（国内比较常见）
三、剽窃（Plagiarism）：窃取他人的想法、过程、结果、文字等，而未给他人的贡献已足够的承认
  盗用他人的物件是偷，盗用他人的文字也是偷
不包括：能力不足的错误和观点的分歧
  这一点往往导致法律和道德上的争议

## Slide 4: 剽窃的5个层次（摘自IEEE指南）
最严重地是未注明出处地全文复制一篇论文
  吊销违规者在IEEE刊物上的发表权利5年
其次是未注明出处地大量复制一篇论文，达一半的篇幅
  处罚和上面的是一样的
第三是未注明出处地照搬句子、段落或插图
第四是未注明出处地不恰当地复述整页或整段内容，通过改变个别单词、词组或重排句子顺序
最后是注明出处地复制一篇论文的很大一部分，而没有清楚地表明谁做了或写了什么

## Slide 5: 抄别人的描述，把数据换成自己的, OK?
“因为英文水平有限，所以我写英文文章时借鉴了那些母语为英语的同行发表的相关文章，甚至原封不动地摘抄了一些语句，这是我个人的问题，以后我肯定会多加注意！
与文科类文献不同，即使在化学专业学术论文中原封不动地借鉴了文献中的某些语句，但只要报道的是自己的研究结果和结论，就和抄袭没有任何关系！因为化学文献注重的是实验方法、数据和结论，而不是个别单词或者语句的写法。”

## Slide 6: 剽窃与引用
你用了别人的大段文字，注明了出处，但是没有对别人的文字做恰当的改写，也是剽窃
  如果是直接引用别人的文字，要用引号给引起来表示是引用，光是注明出处还不行
    有的人写论文的引言部分去抄别人的，抄完了注明引自这篇论文。那也是剽窃
重要、重要、重要……
  你在介绍别人的成果的时候，必须用自己的语言进行复述，而不能不用引号地直接用别人的话
    这是国际学术界公认的一条准则

## Slide 7: 署名、一稿多投和会议转杂志
导师署名：你既然署了名，就要承担责任
  署名是一种荣誉，也是一种责任
  不能说好事都归你，坏事就都不负责
学术行为不当中还有一种情况：一稿多投
  原因：看了新文章，没有新收获
  一稿多投在国际上被认为是不正当的行为
  国际学术期刊一般都是反对一稿多投的
会议转杂志，一般会有一个修改比例
  例如：正文内容有30%以上不同
  国内会议和多数杂志没有这个要求
一稿多投？没有完全禁止！

## Slide 8: 一稿多投的“技巧”：不当行为
一次投多个刊物：刊物文章的组织带来不便
  提高命中率
  挑选高档次
  挑选能够快速发表的
在国外刊物和国内刊物同时一稿多投
国外转国内：外文发表后又翻译成中文发表
  纯粹就是为了增加论文数
“遍地开花”大法
  题目、摘要、正文修改数个字
  一稿三投、四投、……、十五投

## Slide 9: 发现抄袭和一稿多投的利器
提供论文相似度对比的网站
  原始目的：为研究者提供关相关研究的查找
  英文网站：
  中文网站：CNKI（中国知网）、军网
    知网节技术
  不足：跨语种机器难以识别，“反相似”的处理……
打击学术不端行为的网站
  新语丝

## Slide 10: Advanced Computer Architecture 2017
Dr. Chun-yuan ZHANG
College of Computer, NUDT
Fall, 2017

## Slide 11: Processor Examples

## Slide 12: First of All, We Ought to Know What We have Done
Why electronic computer?
What is the road and who are the pioneers?
What is the elements or the base of building a computer?
What is the near future look like?
What is your chance?
  This is what I really out of my imagenation!

## Slide 13: Where It Came From?
1940 - PN junction
Russel Ohl at Bell Labs develops the PN junction that produces 0.5 volts when exposed to light

## Slide 14: Point Contact Transistor

## Slide 15: Junction Transistor
The point contact transistor was difficult to produce and was replaced by the junction transistor by the mid fifties
In 1956 the importance of the invention of the transistor by Bardeen, Brattain and Shockley was recognized by the Nobel Prize in physics

## Slide 16
http://www.nobelprize.org/
In 1951,the junction transistor was developed

## Slide 17
http://www.nobelprize.org/
In July of 1958, Jack Kilby was a recent hire at Texas Instruments
On July 24, 1958 in the quiet of the miniaturization lab…

## Slide 18: The 1st Planar IC
By late 1958 Swiss-born physicist - Jean Hoerni at Fairchild had developed a structure with N and P junctions formed in silicon.
  Over the junctions a thin layer of silicon dioxide was used as an insulator and holes were etched open in the silicon dioxide to connect to the junctions
Czech-born physicist - Kurt Lehovec of Sprague Electric developed the technique of using PN junctions to electrically isolate components
In 1959, Robert Noyce also of Fairchild had the idea to create an integrated circuit by combing Hoerni's and Lehovec's processes and evaporating a thin metal layer over the circuits
  The metal layer connected down to the junctions through the holes in the silicon dioxide and was then etched into a pattern to interconnect the circuit

## Slide 19: Hard Disk

## Slide 20
Optical Fiber

## Slide 21
Electronic Properties (wikipedia)

## Slide 22
法国科学研究中心（CNRS, The French National Center for Scientific Research ）
美国国家标准技术研究所（NIST, National Institute of Standards and Technology）
http://www.nobelprize.org/

## Slide 23: Next...
Processor Examples
1. The ARM Cortex-A8 ...

## Slide 24: ARM Cortex-A8
the ARM Cortex-A8 core is used
  Apple A9 processor in the iPad, as well as the processor in the Motorola Droid and the iPhones 3GS and 4
The A8 is a dual-issue, statically scheduled superscalar
  with dynamic issue detection, which allows the processor to issue one or two instructions per clock

## Slide 25: The A8 Dynamic Branch Predictor
A 512-entry two-way set associative branch target buffer (BTB)
A 4K-entry global history buffer (BPB)
  Indexed by the branch history and the current PC
  In the event that the branch target buffer misses, a prediction is obtained from the global history buffer, which can then be used to compute the branch address
An eight-entry return stack is kept to track return addresses
An incorrect prediction results in a 13-cycle penalty as the pipeline is flushed

## Slide 26: The Five-stage Instruction Decode of The A8

## Slide 27: The Five-stage Instruction Decode of The A8
In the first stage, a PC produced by the fetch unit (either from the branch target buffer or the PC incrementer) is used to retrieve an 8-byte block from the cache
Up to two instructions are decoded and placed into the decode queue; if neither instruction is a branch, the PC is incremented for the next fetch
Once in the decode queue, the scoreboard logic decides when the instructions can issue
In the issue, the register operands are read; recall that in a simple scoreboard, the operands always come from the registers
The register operands and opcode are sent to the instruction execution portion of the pipeline

## Slide 28: The Execution Pipeline for The A8 Processor

## Slide 29: The Execution Pipeline for The A8 Processor
Either instruction 1 or instruction 2 can go to the load/store pipeline
Fully bypassing is supported among the pipelines
The ARM Cortex-A8 pipeline uses a simple two-issue statically scheduled superscalar to allow reasonably high clock rate with lower power

## Slide 30: Performance of the A8 Pipeline
The A8 has an ideal CPI of 0.5 due to its dual-issue structure
Pipeline stalls can arise from three sources
  1. Functional hazards
  2. Data hazards, which are detected early in the pipeline and may stall either both instructions or the second of a pair
    If the first cannot issue, the second is always stalled
    The compiler is responsible for preventing such stalls when possible
  3. Control hazards, which arise only when branches are mispredicted

## Slide 31: The Estimated of The CPI on The ARM A8

## Slide 32: The Performance Ratio for The A9 Compared to The A8
Both using a 1 GHz clock and the same size caches for L1 and L2
The A9 is about 1.28 times faster

## Slide 33: ARM Cortex-A9
The ARM Cortex-A9 is a dynamically scheduled superscalar processor
The A9, like the A8, issues up to two instructions per clock, but it uses dynamic scheduling and speculation
Up to four pending instructions (two ALUs, one load/store or FP/multimedia, and one branch) can begin execution in a clock cycle
The A9 uses a more powerful branch predictor, instruction cache prefetch, and a nonblocking L1 data cache

## Slide 34: Next…
Example 2: PowerPC 604e

## Slide 35: PowerPC 604e, Introduced in 1996
Manufactured by IBM and Motorola respectively
separate 32 KB data and instruction L1 caches
5.1 million transistors on a 0.35 µm fabrication process
The die was 148 mm² or 96 mm² large, drawing 16-18W at 233 MHz
Operated at speeds between 166 and 233 MHz and supported a memory bus up to 66 MHz

## Slide 36: PowerPC 604e : Features
The PowerPC 604e includes we have discussed
  Four-way superscale: ability to fetch, issue and complete up to four instructions per cycle
  Dynamic branch prediction
  Speculation
  Out-of-order execution
The Tomasulo's algorithm, speculation extended
  The 604e has seven separate execution units, each of which can initiate execution independently from its own reservation stations

## Slide 37: The Seven Function Units 1/2
Two separate simple integer units (XSU0 and XSU1) for add, sub, etc
  One cycle per simple operation
One complex integer unit (MCFXU) for integer multiply/divide
  3-20 cycles per operation
One condition register unit
One branch processing unit (BPU)

## Slide 38: The Seven Function Units 2/2
One load/store unit (LSU)
  One cycle per integer loads
  Two cycles per FP loads
One floating-point unit (FPU)
  Two cycles for FP add, multiply, or multiply/add
  31 cycles for FP divide
The 604e pipeline varies from 5 to 7 clock cycles
  Instructions like divide take longer

## Slide 39: Block Diagram

## Slide 40: PowerPC 604e : Reorder Buffer
The reorder buffer does not hold speculative results
  It only holds the information needed to complete the instruction when it commits
The register sets (both GPRs and FPRs) are extended with 8 extra registers in each set
  These extra registers are used to hold the speculative results until the instruction commits
  At which time the results are written from these “renaming” registers to the standard registers
All operands still are loaded into reservation stations as soon as they are available

## Slide 41: Pipeline Stages : Fetch
The fetch unit
  Loads the instruction queue in the dispatch unit with instructions from the i-cache
  Determines the next PC
A 256-entry BTB is used as the first source for predicting the next address
Another 2048-entry BPB is used when there is no hit in the BTB
  But a branch is decoded
Still another stack of return address registers is used to predict subroutine returns
  This is the indirect branch processing unit

## Slide 42: Pipeline Stages : Instruction Decode
The next four instructions are decoded in this stage and passed on to the issue stage

## Slide 43: Pipeline Stages : Instruction Issue
The instructions are issued to the appropriate reservation stations during this stage
  The 604e calls this operation dispatch
An entry in the reorder buffer is allocated to ensure in-order completion
Operands are read from the register file and passed to either the functional unit or into the reservation station
A rename register is allocated to hold the result of the instruction

## Slide 44: Pipeline Stages : Execute 1/2
Only when all operands are available in a reservation station
At the end of execution, the result is written on the appropriate result bus(CDB)
  An execution can take from 1 to 31 cycles
The waiting reservation stations and rename buffer (renaming registers) get the result from the bus
The completion unit is notified that the instruction completed

## Slide 45: Pipeline Stages : Execute 2/2
If it is a mispredicted branch
  Notifying the instruction unit and the completion unit
  Causing instruction fetch to restart at the corrected address
  Causing the completion unit to discard any speculated instructions
  Free the renaming registers holding the speculated results

## Slide 46: Pipeline Stages : Commit
This occurs when all previous instructions have been committed
The results in the rename registers are written to the standard registers and the rename registers are freed
Upon completing a store instruction, the load/store unit is also notified so the corresponding store buffer can be sent to the data cache

## Slide 47: Next…
Intel P6 Architecture

## Slide 49: x86 Microarchitectures, Released
8086: the first 16-bit processor
i186: a SoC like 8086
i286: the first 16-bit VM processor with 24-bit address
i386: the first 32-bit x86 processor
i486: Intel's second-generation of 32-bit x86 processors with RISK technology
P5: Original Pentium microprocessors, two-way superscale integer pipeline, named U and V
P6: Used in Pentium Pro, Pentium II, Pentium II Xeon, Pentium III, and Pentium III Xeon microprocessors

## Slide 50: x86 Microarchitectures, Released and Current
NetBurst: Used in Pentium 4, Pentium D, and some Xeon microprocessors
  Pentium M -- Updated version of Pentium III's P6 microarchitecture designed from the ground up for mobile computing
  Enhanced Pentium M -- Updated, dual core version of the Pentium M microarchitecture used in Core microprocessors.
Core: New microarchitecture, based on the P6 architecture, used in Core 2 and Xeon microprocessors, built on a 65nm process.
  Penryn: 45nm shrink of the Core microarchitecture with larger cache, faster FSB and clock speeds, and SSE4.1 instructions.
Atom: Low-power, in-order x86-64 processor for use in Mobile Internet Devices
Nehalem: was released in 2008, built on a 45nm process
  It will be an enhanced version of the Core microarchitecture

## Slide 51: x86 Multiprocessor: Xeon Phi (Wikipedia)
Intel Many Integrated Core Architecture or Intel MIC (pronounced Mike) is a multiprocessor computer architecture developed by Intel incorporating earlier work on the Larrabee many core architecture, the Teraflops Research Chip multicore chip research project and the Intel Single-chip Cloud Computer multicore microprocessor
Larrabee: Multi-core in-order x86-64 processor with wide SIMD vector units and texture sampling hardware for use in graphics
  See also: Larrabee (microarchitecture), Teraflops Research Chip, and Single-chip Cloud Computer
Intel MIC (Redirected from Xeon Phi)

## Slide 52: Intel P6: the 6th Generation Microarchitecture
The first implementation of the P6 core was the Pentium Pro CPU in 1995
  From Pentium Pro to Pentium III
    It was succeeded by the NetBurst in 2000
  Revived in the Pentium M line of microprocessors
    The successor to the Pentium M variant of the P6 is the Intel Core microarchitecture
    Intel has found that the superpipelined NetBurst pipelines and eneygy efficiency are lower then P6

## Slide 53: Intel P6 Charactors
The P6 is a CISC/RISC hybrid
The Pentium Pro, Pentium II, Pentium III
  A CISC instruction sets
  A RISC micro-architecture as a core
The Pentium Pro and Pentium II were developed by the company’s design team in Hillsboro, Oregon
  They earlier worked on the i960, a RISC design
  Previous x86 Intel processors came from their facility in Santa Clara, CA

## Slide 54: The First P6: Pentium Pro (on November 1995)
L1 cache: 8 + 8 KB (Data + Instructions)
L2 cache: 256, 512 KB (one die) or 1024 KB (two 512 KB dies) in a multi-chip module clocked at CPU-speed
Socket: Socket 8
Front side bus: 60 and 66 MHz
VCore: 3.1-3.3 V
Fabrication: 0.50 µm or 0.35 BiCMOS
Transistors: 5.5 million
Clockrate: 150, 166, 180, 200 MHz

## Slide 55: Pentium Pro

## Slide 56: Pentium II (on May 7, 1997)
Produced: From mid 1997 to early 1999
Max CPU clock: 233 MHz to 450 MHz
FSB speeds: 66 to 100
Min feature size: 0.35 µm to 0.25 µm
Instruction set: x86, MMX
Socket(s): Slot 1
VCore: 1.5, 1.55, 1.6 V, 2.0 V, 2.8 V
Transistors: 7.5 million
Others
  Core name(s): Klamath, Deschutes, Tonga, Dixon
  In early 1999, it was superseded by the Pentium III

## Slide 57: Pentium II, Slot 1

## Slide 58: The Intel P6 Competitors
Using a RISC core for the x86 architecture is not original to Intel
Similar designs appeared earlier in
  The NextGen Nx586 -> AMD K6
  The AMD K5
  The Cyrix 6x86 and MII -> National Semiconductor -> VIA C
  IDT WinChip -> VIA

## Slide 59: Intel P6 Organization
A three-issue, superscalar micro-architecture
A 14-stage pipeline
  Intel sometimes counts them as 12 stages
Six parallel execution units
  Two integer
  One load
  One store
  One FP unit
  One MMX unit
    The first separate MMX unit processor

## Slide 60: The Latency and Repeat Rate For uOPs
Instruction name | Pipeline stages | Repeat rate
Integer ALU | 1 | 1
Integer load | 3 | 1
Integer multiply | 4 | 1
FP add | 3 | 1
FP multiply | 5 | 2
FP divide (64-bit) | 32 | 32

## Slide 61: P6 Microarchitecture
Instruction Fetch Unit
BTB/BAC
Instruction Fetch Unit
Bus interface unit
Instruction
Decoder
Instruction
Decoder
Register Alias Table
Allocator
Microcode Sequencer
Reservation Station
ROB & Retire RF
AGU
MMX
IEU/JEU
IEU/JEU
FEU
MIU
Memory Order Buffer
Data Cache Unit (L1)
External bus
Chip boundary
Control
Flow
Restricted
Data
Flow
Instruction Fetch Cluster
Issue Cluster
Out-of-order
Cluster
Memory
Cluster
Bus Cluster

## Slide 62: Intel P6 : Stage 1
The instruction fetch unit (IFU) calculates the value of the next PC
The 512 entry BTB helps the IFU choose an instruction address
  If the updated PC points to a recently used branch instruction
  Whether or not that branch is predicted to be taken or not

## Slide 63: Intel P6 : Stages 2-4 1/3
The IFU fetches two cache lines of 128 bits each from the instruction cache during these three stages
I-cache fetches are pipelined with a new instruction line fetch starting on every cycle

## Slide 64: Intel P6 : Stages 2-4 2/3
A miss in the 16KB I-cache causes the hardware to go back to the L2 cache
  L2 can fetch 2 x 64 bits every 2 cycles
Two I-cache lines are fetched by the IFU
  The x86 instructions can be long (up to 120 bits) and may wrap from one cache line to another

## Slide 65: Intel P6 : Stages 2-4 3/3
The IFU marks the boundary of each instruction
Passes 16 aligned bytes to the decoder
Three decoders, working in parallel, convert x86 instructions into micro-ops

## Slide 66: Intel P6 : Stages 5-6 Decoder 1/2
Two decoders handle simple instructions (mostly integer operations) and generate 1 micro-op per cycle
One decoder handles more complex instructions and generates up to 4 micro-ops per cycle

## Slide 67: Intel P6 : Stages 5-6 Decoder 2/2
Attach flags and status bits to prepare for the out-of-order execution
Some x86 instructions are too complex for the decoders
  Passed to the micro-code instruction sequencer, which corresponds to the micro-code ROM in early x86 chips

## Slide 68: Intel P6 : Micro-ops 1/2
Have a fixed length of 118 bits
  A very long instruction?
Contain an operation and three operands
  Two sources and a destination
  Each source and destination field has 32-bits, enough to hold a result
    Like a buffer, or a temporary variable

## Slide 69: Intel P6 : Micro-ops 2/2
Use a load/store model
  So an x86 instruction that operates on memory is broken into a sequence of load, ALU, and store micro-ops
Many x86 instructions will translate into a single micro-op
The average will be 1.5 to 2.0 micro-ops per x86 instruction

## Slide 70: X86 Instruction Decoder
4-1-1 decoder
Decode rate depends on instruction alignment
DEC1: translate x86 into micro-operation’s (ops)
DEC2: move decoded ops to ID queue
MS performs translations either
  Generate entire op sequence from microcode ROM
  Receive 4 ops from complex decoder, and the rest from microcode ROM
complex
(1-4)
simple
(1)
simple
(1)
IFU3
Micro-instruction sequencer (MS)
Instruction decoder queue
(6 ops)
Next 3 inst | #Inst to dec
S,S,S | 3
S,S,C | First 2
S,C,S | First 1
S,C,C | First 1
C,S,S | 3
C,S,C | First 2
C,C,S | First 1
C,C,C | First 1
S: Simple
C: Complex

## Slide 71: Intel P6 : Stage 7 1/4
The register renaming occurs
  Using the register alias table (RAT)
The micro-ops pass through the reorder buffer (ROB) on their way to the reservation station
  The ROB logs each micro-op (at stage 8) so it can later be retired in program order

## Slide 72: Intel P6 : Stage 7 2/4
Each of the 40 ROB entries has room to store the result of a load or a calculation
References to the real x86 registers (GPRs and FPRs) are reassigned by the RAT to ROB entries
  Whenever there is a dependency and the real register cannot be used

## Slide 73: Intel P6 : Stage 7 3/4
The ROB gives an extra 40 physical registers
Any of the entries in the ROB can represent the logical register that x86 programs expect to see
40 entries are wide enough to hold integer or FP values as well as some status bits that are added in stage 8

## Slide 74: Intel P6 : Stage 7 4/4
As each micro-op executes
  It reads its data from either the register file or the ROB
  It writes its results to the ROB or the memory order buffer (MOB)
The ROB is implemented as a 40-entry array of content-addressable memory (CAM) that is arranged in a FIFO buffer

## Slide 75: Intel P6 : Stage 8 1/2
The status bits that record the state of each micro-op are added to the registers in the reorder buffer (ROB)
Up to three micro-ops can be renamed and logged in the ROB on each cycle
  These three then flow into the reservation station

## Slide 76: Intel P6 : Stage 8 2/2
Additional bits define
  Which execution unit can handle this micro-op
  If the instruction contains a dependency
  A time stamp
  Branch information
    Including the target and fall through addresses

## Slide 77: Intel P6 : Stage 9, 10 and 11 1/3
Out-of-order execution of the micro-ops occur
The reservation station (RS) holds 20 micro-ops
  The micro-ops wait in the RS until their source operands are all available
  Any micro-ops with all operands available are marked as ready

## Slide 78: Intel P6 : Stage 9, 10 and 11 2/3
Each cycle, up to 6 micro-ops can be dispatched
  Two calculations
  A load
  A store
  A MMX
  A store address

## Slide 79: Intel P6 : Stage 9, 10 and 11 3/3
There are some hardware restrictions on the micro-ops that can be dispatched together
  One FP unit
  Dual-ported data cache

## Slide 80: The Characteristics of the Execution Units 1/3
The integer units
  Add/subtract in 1 cycle
  Multiply in 4 cycles
  Divide in 12-36 cycles
The FP unit
  Adds in 3 cycles
  Multiplies in 5 cycles

## Slide 81: The Characteristics of the Execution Units 2/3
These units are pipelined
  The add and multiply can be executed in parallel
The two address generation units each have 4-input adders to handle x86 addressing

## Slide 82: The Characteristics of the Execution Units 3/3
The ROB can accept three results per cycle
  One from each of the two arithmetic units
  One from a load micro-op
After a micro-op writes its results to the ROB or the MOB, it is eligible to be retired

## Slide 83: Intel P6 : Stages 12, 13 and 14 1/2
After a micro-op has executed, it is returned to the ROB with its status flag changed to show completion
The ROB will retire up to three micro-ops per cycle, always in program order, by writing their results to the register file
  The ROB uses the time-stamp field to retire micro-ops in order

## Slide 84: Intel P6 : Stages 12, 13 and 14 2/2
If an exception occurs, the uncommitted results in the ROB are flushed
  As if the instructions had executed in order up to the point of the exception

## Slide 85: Intel P6 : Pipeline Summary

## Slide 86: P6: Instruction Flow

## Slide 87: P6: Another Point of View

## Slide 88: Next ...
Example: Intel Pentium 4

## Slide 89: Intel Pentium 4
400 MHz System
Bus
Rapid
Execution
Engine
Execution
Trace Cache
Hyper
Pipelined Technology
Advanced
Transfer
Cache
Advanced Dynamic Execution
Streaming
SIMD Extensions 2
Enhanced Floating
Point / Multi-Media

## Slide 90: Intel® Pentium® 4 Processor Design Goals
Two main goals
  Deliver world class performance across both existing and emerging applications
  Deliver performance headroom and scalability for the future
Micro-architecture that will drive performance leadership for the next several years
Processor | Clock Speed (MHz) | Intro Date | Process (micron) | Transistors (million)
Pentium 4 | 1.4G-2G | 2000.11 | 0.18 | 42
Pentium 4 HT | 3.06G | 2002.11 | 0.13 | 55

## Slide 91: P5, P6 & NetBurst: Hyper-Pipelined = Higher Frequency
Basic Pentium Pro Pipeline
Basic Pentium® 4 Processor Pipeline
PREF
DEC
DEC
EXEC
WB
P5 Microarchitecture
IFU1
IFU2
IFU3
DEC1
DEC2
RAT
ROB
DIS
EX
RET1
RET2
P6 Microarchitecture
TC NextIP
TC Fetch
Drive
Alloc
Queue
Rename
Schedule
Dispatch
Reg File
Exec
Flags
Br Ck
Drive
NetBurst Microarchitecture
Basic Pentium Pipeline

## Slide 92: NetburstTM Micro-architecture Pipeline vs P6
1
2
3
4
5
6
7
8
9
10
Fetch
Fetch
Decode
Decode
Decode
Rename
ROB Rd
Rdy/Sch
Dispatch
Exec
Basic P6 Pipeline
Basic Pentium® 4 Processor Pipeline
1
2
3
4
5
6
7
8
9
10
11
12
TC Nxt IP
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
Intro at
³ 1.4GHz
.18µ
Intro at
733MHz
.18µ

## Slide 93: Pentium 4 Microarchitectue
front-end BTB
(4k entries)
I-TLB/Prefetcher
IA32 Decoder
Execution Trace Cache
(12K uops)
Trace Cache BTB
(512~4K entries)
Code ROM
op Queue
Allocator / Register Renamer
Memory op Queue
FP RF / Bypass Ntwk
FP
MMX
SSE/2
L1 Data Cache (8KB 4-way, 64B line, WT, 1rd+1wr port)
Quad
Pumped
400/533MH
3.2/4.3GB/s
BIU
U-L2 Cache
256KB 8-way
128B line, WB,
48GB/s@1.5GHz
256 bits, Core CLK
64 bits, Core clock
100/133MHz
64-bit
System
Bus
2x ALU
2x ALU
Slow ALU
Simple
Inst.
Simple
Inst.
Complex
Inst.
FP Move
AGU
AGU
Ld addr
St addr
FP scheduler
General FP FP mem
INT / FP op Queue
INT Register File/Bypass Network
INT scheduler
Slow INT Fast INT Fast INT memory

## Slide 94: Pentium 4 Block Diagram
L2 Cache and Control
FP RF
FMul
FAdd
MMX
SSE
FP move
FP store
3.2 GB/s System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
Store
AGU
Load
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
uCode
ROM
3
3
Decoder
BTB & I-TLB

## Slide 95: Hyper Pipelined Technology 1/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP: Trace cache next instruction pointer
Pointer from the BTB, indicating location of
next instruction.
2
TC Nxt IP
1

## Slide 96: Hyper Pipelined Technology 2/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
TC Fetch: Trace cache fetch
Read the decoded instructions (uOPs) out of
the Execution Trace Cache
Trace Cache
Notes: Primary instruction cache.

## Slide 97: Hyper Pipelined Technology 3/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Drive: Wire delay
Drive the uOPs to the allocator

## Slide 98: Hyper Pipelined Technology 4/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Alloc: Allocate
Allocate resources required for execution. The
resources include Load buffers, Store buffers, etc..
Rename/Alloc

## Slide 99: Hyper Pipelined Technology 5/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Rename: Register renaming
Rename the logical registers (EAX) to the physical
register space (128 are implemented).
Rename/Alloc

## Slide 100: Hyper Pipelined Technology 6/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Que: Write into the uOP Queue
uOPs are placed into the queues, where they
are held until there is room in the schedulers
uop Queues
Notes: The combination of the uOP queues and the schedulers are analogous to P6’s reservation stations.
This is the last part of the in order machine.

## Slide 101: Hyper Pipelined Technology 7/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Sch: Schedule
Write into the schedulers and compute
dependencies. Watch for dependency to resolve.
Schedulers
Notes: Heart of the out of order machine. Traffic cops making sure that uOPs execute in the right order.

## Slide 102: Hyper Pipelined Technology 8/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Disp: Dispatch
Send the uOPs to the appropriate
execution unit.

## Slide 103: Hyper Pipelined Technology 9/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
RF: Register File
Read the register file. These are the source(s)
for the pending operation (ALU or other).
Integer RF
FP RF
Notes: Includes bypassing from things just finishing execution.

## Slide 104: Hyper Pipelined Technology 10/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Ex: Execute
Execute the uOPs on the appropriate
execution port.
Fop
Fms
AGU
AGU
ALU
ALU
ALU
ALU

## Slide 105: Hyper Pipelined Technology 11/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Flgs: Flags
Compute flags (zero, negative, etc..). These
are typically the input to a branch instruction.
ALU
ALU
ALU
ALU

## Slide 106: Hyper Pipelined Technology 12/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Br Ck: Branch Check
The branch operation compares the result of the
actual branch direction with the prediction.
ALU
ALU
ALU
ALU

## Slide 107: Hyper Pipelined Technology 13/13
FP RF
Fop
Fms
System Interface
L2 Cache and Control
L1 D-Cache and D-TLB
AGU
AGU
Schedulers
Integer RF
ALU
ALU
ALU
ALU
Trace Cache
Rename/Alloc
uop Queues
BTB
ROM
3
3
Decoder
BTB & I-TLB
L2 Cache and Control
2
3
4
5
6
7
8
9
10
11
12
TC Fetch
Drive
Alloc
Rename
Que
Sch
Sch
Sch
13
14
Disp
Disp
15
16
17
18
19
20
RF
Ex
Flgs
Br Ck
Drive
RF
TC Nxt IP
1
Drive: Wire delay
Drive the result of the branch check to the front
end of the machine.

## Slide 108: The Intel Core i7: Nehalem Architecture
The i7 uses an aggressive out-of-order speculative microarchitecture
  With reasonably deep pipelines
  With the goal of achieving high instruction throughput
  By combining multiple issue
  And high clock rates
The total pipeline depth is 14 stages
  branch mispredictions costing 17 cycles
There are 48 load and 32 store buffers
The six independent functional units can each begin execution of a ready micro-op in the same cycle

## Slide 109
Cache
Micro-OP
Handling
Micro-OP
Decode and
loop stream
detect
New or
Improved in
Nehalem

## Slide 110: i7 Pipeline Steps 1: Instruction Fetch
The processor uses a multilevel branch target buffer to achieve a balance between speed and prediction accuracy
There is also a return address stack to speed up function return
  Mispredictions cause a penalty of about 15 cycles
Using the predicted address, the instruction fetch unit fetches 16 bytes from the instruction cache

## Slide 111: i7 Pipeline Steps 2: Placed in the Predecode Instruction
The 16 bytes are placed in the predecode instruction buffer
a process called macro-op fusion is executed
  Macro-op fusion takes instruction combinations such as compare followed by a branch and fuses them into a single operation

## Slide 112: i7 Pipeline Steps 2: Placed in the Predecode Instruction
The predecode stage also breaks the 16 bytes into individual x86 instructions
  This predecode is nontrivial since the length of an x86 instruction can be from 1 to 17 bytes and the predecoder must look through a number of bytes before it knows the instruction length
Individual x86 instructions (including some fused instructions) are placed into the 18-entry instruction queue

## Slide 113: i7 Pipeline Steps 3: Micro-op Decode
Individual x86 instructions are translated into micro-ops
  Micro-ops are simple MIPS-like instructions that can be executed directly by the pipeline
  This approach of translating the x86 instruction set into simple operations that are more easily pipelined was introduced in the Pentium Pro in 1997 and has been used since

## Slide 114: i7 Pipeline Steps 3: Micro-op Decode
Three of the decoders handle x86 instructions that translate directly into one micro-op
  For x86 instructions that have more complex semantics, there is a microcode engine that is used to produce the micro-op sequence
  It can produce up to four micro-ops every cycle and continues until the necessary micro-op sequence has been generated
The micro-ops are placed according to the order of the x86 instructions in the 28-entry micro-op buffer

## Slide 115: i7 Pipeline Steps 4: Loop Stream Detection
The micro-op buffer preforms loop stream detection and microfusion
If there is a small sequence of instructions (less than 28 instructions or 256 bytes in length) that comprises a loop, the loop stream detector will find the loop and directly issue the micro-ops from the buffer, eliminating the need for the instruction fetch and instruction decode stages to be activated

## Slide 116: i7 Pipeline Steps 4: Microfusion
Microfusion combines instruction pairs such as load/ALU operation and ALU operation/store and issues them to a single reservation station (where they can still issue independently), thus increasing the usage of the buffer
  In a study of the Intel Core architecture, which also incorporated microfusion and macrofusion, Bird et al. [2007] discovered that microfusion had little impact on performance, while macrofusion appears to have a modest positive impact on integer performance and little impact on floating-point performance

## Slide 117: i7 Pipeline Steps 5: Basic Instruction Issue
Perform the basic instruction issue
  Looking up the register location in the register tables
  Renaming the registers
  Allocating a reorder buffer entry
  And fetching any results from the registers or reorder buffer
Before sending the micro-ops to the reservation stations

## Slide 118: i7 Pipeline Steps 6: to Reservation Station
The i7 uses a 36-entry centralized reservation station shared by six functional units
Up to six micro-ops may be dispatched to the functional units every clock cycle

## Slide 119: i7 Pipeline Steps 7: Execution
Micro-ops are executed by the individual function units and then results are sent back to any waiting reservation station as well as to the register retirement unit, where they will update the register state, once it is known that the instruction is no longer speculative
The entry corresponding to the instruction in the reorder buffer is marked as complete

## Slide 120: i7 Pipeline Steps 8: Commit
When one or more instructions at the head of the reorder buffer have been marked as complete, the pending writes in the register retirement unit are executed, and the instructions are removed from the reorder buffer

## Slide 121: Performance of the i7
A single-thread pipeline performance
The cost of a branch mispredict is 15 cycles
the cost of an L1 miss is about 10 cycles
L2 misses are slightly more than three times as costly as an L1 miss
L3 misses cost about 13 times what an L1 miss costs (130–135 cycles)
  Although the processor will attempt to find alternative instructions to execute for L3 misses and some L2 misses, it is likely that some of the buffers will fill before the miss completes, causing the processor to stop issuing instructions

## Slide 122: The Amount of “Wasted Work”
The ratio of dispatched micro-ops that do not graduate to all dispatched micro-ops

## Slide 123: The CPI for the 19 SPECCPU2006
- An average CPI for 0.83
- In the integer case, the CPI values range from 0.44 to 2.66 with a standard deviation of 0.77
- The FP case is from 0.62 to 1.38 with a standard deviation of 0.25

## Slide 124: The Four-core Intel i7 920, ARM A8 and the Intel Atom 230

## Slide 125: The Relative Performance And Energy Efficiency
the i7 920 is 4 to over 10 times faster than the Atom 230 but that it is about 2 times less power efficient on average!

## Slide 126: Characteristics of Four IBM Power Processors
All except the Power6 were dynamically scheduled, which is static, and in-order, and all the processors support two load/store pipelines. The Power6 has the same functional units as the Power5 except for adecimal unit. Power7 uses DRAM for the L3 cache

## Slide 127: Homework
Textbook
  3.13
Paper
  "The MIPS R10000 Superscalar microprocessor", Yeager, IEEE Micro 16(2), 1996
  https://www.realworldtech.com/jaguar/
References
  https://en.wikipedia.org/wiki/X86
  https://en.wikipedia.org/wiki/List_of_Intel_microprocessors

## Slide 128: Next …
Vector, SIMD and GPU