## Slide 1
Instruction | Opcode | Register | Data/Addr_h | Data/Addr_l
Load R1 257 | 0x00 | 1 | 0x01 | 0x01
Load R2 R1 | 0x01 | 2 | 0x00 | 1
Load R3 $257 | 0x02 | 3 | 0x01 | 0x01
Store R1 $257 | 0x10 | 1 | 0x01 | 0x01
Cmp R1 257 | 0x20 | 1 | 0x01 | 0x01
Cmp R1 R2 | 0x21 | 1 | 0x00 | 2
BEQ label | 0x30 | 0x00 | the addr of label
BNQ label | 0x31 | 0x00 | the addr of label
Add R1 257 | 0x40 | 1 | 0x01 | 0x01
Sub R1 257 | 0x41 | 1 | 0x01 | 0x01
Add R1 R2 | 0x42 | 1 | 0x00 | 2
Sub R1 R2 | 0x44 | 1 | 0x00 | 2
Halt | 0xFE | 0xFE | 0xFE | 0xFE

## Slide 2: Assumption
- 16 bit architecture
- Instructions are 32 wide

## Slide 3: Instruction format
First byte is opcode
  00(0x00) is LOAD
  16(0x10) is STORE
  32(0x20) is CMP
  48(0x30) is BRANCH
Second byte is register
Third and fourth are data

## Slide 4: Load——example
direct Load
  65535 is 0xFFF
  Load R2 65535
  0x00 0x02 0xFF 0xFF
Load from another register
  Load R3 R6
  0x01 0x03 0x00 0x06
Load from memory
  Load R3 0xABCD
  0x02 0x03 0xAB 0xCD

## Slide 5: Missing?
Multipy, Divide, AND, OR, XOR, etc
Subroutines
Stack
More ...

## Slide 6: pseudo code(convert the instruction to Machine code）

## Slide 7: Label
All the Labels start with dot
  .loop
Use directory to save the table of labels
  dic = {loop1:0xABCD, loop2:0xDEFF}
example