## Slide 1: Instruction Set Architecture Design
Designing an ISA is hard:
  How many operations?
  What types of storage, how much?
  How to encode instructions?
  How to future-proof?
How to decide? Take a quantitative approach
  Take a set of representative benchmark programs
  Evaluate version of your ISA
  Pick waht works best overall(performance, energy, area...)
Corollary: Optimize the common case
reference: https://computationstructures.org/lectures/isa/isa.html#17
Notes:   经过几十年的计算机使用，现在有几个标准化的基准套件可供我们使用。
  因此，如果让我来设计ISA，我只能做到一些普遍的指令

## Slide 2: Storage
32 bit architecture
  232 bytes(4 GB of memory)
  230 4-byte words
Instructions are 32 wide
32 registers

## Slide 3: Instructions
Three types of instructions:
  Arithmetic and logical
  Loads and stores
  Branches and compare
All instructions have a fixed length: 32 bits(4 bytes)
  Tradeoff(vs variable-length instructions)
    Simpler, next PC is easy to compute