## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 04 ILP & Loop Unrolling

## Slide 3: How Changes Brustad: Reformation to Revolution
IBM PC
  Personal Computing
  Ad, 11/81
  Giant

## Slide 4
Notes: 8088是4044的改进版，8080是8位，8086是16位，兼容8位，但是硬件不兼容，8088硬件兼容。。。。

## Slide 5: PC inside

## Slide 6: IBM PC, 1981
Hardware
  Team from IBM building PC prototypes in 1979
  Motorola 68000 chosen initially, but 68000 was late
  IBM builds “stopgap” prototypes using 8088 boards from Display Writer word processor
  8088 is 8-bit bus version of 8086 => allows cheaper system
  Estimated sales of 250,000 => 100,000,000s were sold
Software
  Microsoft negotiates to provide OS for IBM
    Later buys and modifies QDOS from Seattle Computer Products
Open System
  Standard processor, Intel 8088
  Standard (hardware) system interfaces => 8088 extension => ISA standard buses
  Standard OS, MS-DOS, PC-DOS, DR-DOS ...
  IBM permits cloning and third-party software

## Slide 7: PC/AT 286

## Slide 8: ILP
ILP -- Instruction Level Parallel
Exploiting ILP Goal
  Minimize CPI
How to?
Pipeline CPI = Ideal pipeline CPI
+ Structural stalls
+ Data hazard stalls
+ Control stalls
Notes: 指令集并行

## Slide 9: The Major ILP Techniques 1/2
Technique | Reduces | Section
Forwarding and bypassing | Potential data hazard stalls | C.2
Delayed branches and simple branch scheduling | Control hazard stalls | C.2
Basic compiler pipeline scheduling | Data hazard stalls | C.2, 3.2
Basic dynamic scheduling (scoreboarding) | Data hazard stalls from true dependences | C.7
Loop unrolling | Control hazard stalls | 3.2
Branch prediction | Control stalls | 3.3
Notes: 这两张表测试学的怎么样

## Slide 10: The Major ILP Techniques 2/2
Technique | Reduces | Section
Dynamic scheduling with renaming | stalls from Data hazard, output dependences and antidependences | 3.4
Hardware speculation | Data hazard and control hazard stalls | 3.6
Dynamic memory disambiguation | Data hazard stalls with memory | 3.6
Issuing multiple instructions per cycle | Ideal CPI | 3.7, 3.8
Compiler dependence analysis, software pipelining, trace scheduling | Ideal CPI, data hazard stalls | H.2, H.3
Hardware support for compiler speculation | Ideal CPI, data hazard stalls, branch hazard stalls | H.4, H.5

## Slide 11: Dependences, Hazard and Stall
Dependence
Hazard
Stall
Notes: 依赖，阻塞，空转

## Slide 12: 3 Type Data Hazards: Regs
Data-dependence
  r3 ← r1 op r2 Read-after-Write
  r5 ← r3 op r4 (RAW) hazard
Anti-dependence
  r3 ← r1 op r2 Write-after-Read
  r1 ← r4 op r5 (WAR) hazard
Output-dependence
  r3 ← r1 op r2 Write-after-Write
  r3 ← r6 op r7 (WAW) hazard

## Slide 13: Data Hazards: An Example
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
Notes: 典型代码

## Slide 14: Data Hazards: RAW Hazards – 1
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
Notes: 写后读

## Slide 15: Data Hazards: RAW Hazards – 2
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 16: Data Hazards: RAW Hazards – 3
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 17: Data Hazards: RAW Hazards – 4
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 18: Data Hazards: WAR Hazards – 1
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 19: Data Hazards: WAR Hazards – 2
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 20: Data Hazards: WAW Hazards – 1
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2

## Slide 21: Data Hazards - All
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
Execuation order
  In-order
  Out-of-order (o-o-o)
I6
I2
I4
I1
I5
I3
Notes: 除法更耗时

## Slide 22: Instruction Scheduling: Valid Orderings
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
I6
I2
I4
I1
I5
I3
in-order | I1 | I2 | I3 | I4 | I5 | I6
o-o-o |  |  |  |  |  | 

## Slide 23: Instruction Scheduling: Out-of-order
I1 FDIV.D f6, f6, f4
I2 FLD f2, 45(x3)
I3 FMUL.D f0, f2, f4
I4 FDIV.D f8, f6, f2
I5 FSUB.D f10, f0, f6
I6 FADD.D f6, f8, f2
I6
I2
I4
I1
I5
I3
in-order | I1 | I2 | I3 | I4 | I5 | I6
o-o-o | I2 | I1 | I3 | I5 | I4 | I6
Notes: l3和l4可能存在结构相关

## Slide 24: Latency of Instructions: Assumption
Latency*
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMUL.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
    *The latencies are extra cycles to the 5-stage

## Slide 25: In-order Issue and In-order Completion
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMUL.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
clk | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
in/in | 1 | 2 |  |  | 1 | 2 | 3 | 4 |  | 3 | 5 | 4 | 6 | 5 | 6
FDIV.D: 123456789 simplified as-> 1234

## Slide 26: In-order Issue and Out-of-order Completion
I1 FDIV.D f6, f6, f4 4
I2 FLD f2, 45(x3) 1
I3 FMUL.D f0, f2, f4 3
I4 FDIV.D f8, f6, f2 4
I5 FSUB.D f10, f0, f6 1
I6 FADD.D f6, f8, f2 1
clk | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
in/out | 1 | 2 | 2 | 3 | 1 | 4 | 3 | 5 | 5 | 4 | 6 | 6 |  |  | 
Notes: 输出允许乱序时

## Slide 27: Usage:
Loop Unrolling
& Instruction Scheduling

## Slide 28: Assumptions
5-stage integer pipeline
FUs are fully pipelined or replicated
Branches delay: 1 clock cycle
Conditions delay: 1 clock cycle
An integer ALU operation latency of 0

## Slide 29: The Revised Pipelined (Lecture 02)
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 30: Control Hazard on Branches
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Notes: 分支指令造成的延迟

## Slide 31: Latencies of FP Operations
Instruction producing result | Instruction using result | Latency in cycles
FP ALU op | Another FP ALU op | 3
FP ALU op | Store double | 2
Load double | FP ALU op | 1
Load double | Store double | 0

## Slide 32: Code Translate
for (i=999; i>=0; i=i–1)
x[i] = x[i] + s;

## Slide 33: Code Translate
Loop: fld f0,0(x1) //f0=array element
fadd.d f4,f0,f2 //add scalar in f2
fsd f4,0(x1) //store result
addi x1,x1,8 //decrement pointer
//8 bytes (per DW)
bne x1,x2,Loop //branch x1 != x2
R1: initially highest address of the array
R2: pre-computed to last element address - 8

## Slide 34: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)

## Slide 35: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | ? fadd.d f4,f0,f2
Load double used by a FP ALU op, the Latency in 1 cycle

## Slide 36: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2

## Slide 37: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | ? fsd f4,0(x1)
a FP ALU op used by a Store double , the Latency in 2 cycle

## Slide 38: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | ? fsd f4,0(x1)
a FP ALU op used by a Store double , the Latency in 2 cycle
This is the second

## Slide 39: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
a FP ALU op used by a Store double , the Latency in 2 cycle
there are two stall cycles

## Slide 40: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | ? addi x1,x1,8

## Slide 41: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | addi x1,x1,8

## Slide 42: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | addi x1,x1,8
8 | ? bne x1,x2,Loop

## Slide 43: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | addi x1,x1,8
8 | Stall
9 | bne x1,x2,Loop
what is the next?

## Slide 44: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | addi x1,x1,8
8 | Stall
9 | bne x1,x2,Loop
10 | ?

## Slide 45: The Loop Execution Without Scheduling
Clock | Unscheduled
1 | fld f0,0(x1)
2 | Stall
3 | fadd.d f4,f0,f2
4 | Stall
5 | Stall
6 | fsd f4,0(x1)
7 | addi x1,x1,8
8 | Stall
9 | bne x1,x2,Loop
10 | Stall

## Slide 46: The Loop Execution Without Scheduling
10 clock cycles an iteration
Just 3 for execution (fld, fadd.d, fsd)
  30%
  5 clock cycles of stall (50%)
  2 for loop overhead (20%)
Rewrite code to minimize stalls?

## Slide 47: Focus, 👀, Focus: Rewrite the Code!
Clk | Unscheduled | scheduled
1 | fld f0,0(x1) | fld f0,0(x1)
2 | Stall | 
3 | fadd.d f4,f0,f2 | 
4 | Stall | 
5 | Stall | 
6 | fsd f4,0(x1) | 
7 | addi x1,x1,8 | 
8 | Stall | 
9 | bne x1,x2,Loop | 
10 | Stall | 

## Slide 48: Scheduling the Loop 1/4
Clk | Unscheduled | scheduled
1 | fld f0,0(x1) | fld f0,0(x1)
2 | Stall | addi x1,x1,8
3 | fadd.d f4,f0,f2 | 
4 | Stall | 
5 | Stall | 
6 | fsd f4,0(x1) | 
7 | addi x1,x1,8 | 
8 | Stall | 
9 | bne x1,x2,Loop | 
10 | Stall | 

## Slide 49: Scheduling the Loop 2/4
Clk | Unscheduled | scheduled
1 | fld f0,0(x1) | fld f0,0(x1)
2 | Stall | addi x1,x1,8
3 | fadd.d f4,f0,f2 | fadd.d f4,f0,f2
4 | Stall | 
5 | Stall | 
6 | fsd f4,0(x1) | 
7 | addi x1,x1,8 | 
8 | Stall | 
9 | bne x1,x2,Loop | 
10 | Stall | 

## Slide 50: Scheduling the Loop 3/4
Clk | Unscheduled | scheduled
1 | fld f0,0(x1) | fld f0,0(x1)
2 | Stall | addi x1,x1,8
3 | fadd.d f4,f0,f2 | fadd.d f4,f0,f2
4 | Stall | ? Stall
5 | Stall | ? Stall
6 | fsd f4,0(x1) | fsd f4,0(x1)
7 | addi x1,x1,8 | 
8 | Stall | 
9 | bne x1,x2,Loop | 
10 | Stall | 

## Slide 51: Scheduling the Loop 4/4
Clk | Unscheduled | scheduled
1 | fld f0,0(x1) | fld f0,0(x1)
2 | Stall | addi x1,x1,8
3 | fadd.d f4,f0,f2 | fadd.d f4,f0,f2
4 | Stall | Stall
5 | Stall | bne x1,x2,Loop
6 | fsd f4,0(x1) | fsd f4,0(x1)
7 | addi x1,x1,8 | 
8 | Stall | 
9 | bne x1,x2,Loop | 
10 | Stall | 
Notes: 分支槽中的指令是必须执行的

## Slide 52: The Loop With and Without Scheduling
6 clock cycles an iteration
The speedup is 10/6=1.7
Still just 3 for execution (fld, fadd.d, fsd)
  50%
  1 clock cycle of stall (17%)
  2 clock cycles for loop overhead (33%)
How to minimize stalls and get rid of the overhead cycles?
Notes: 编译器的指令优化

## Slide 53: Loop Unrolling
Omit Control Overhead and Stall

## Slide 54: Loop Unrolled Code
Loop: fld f0,0(x1)
fadd.d f4,f0,f2
fsd f4,0(x1) //drop addi & bne
fld f6,8(x1)
fadd.d f8,f6,f2
fsd f8,8(x1) //drop addi & bne
fld f0,16(x1)
fadd.d f12,f0,f2
fsd f12,16(x1) //drop addi & bne
fld f14,24(x1)
fadd.d f16,f14,f2
fsd f16,24(x1)
addi x1,x1,32
bne x1,x2,Loop
Notes: 寄存器增加

## Slide 55: Loop Unrolled Code: Exec Time
 |  |  | start waiting, …,execute
 | Loop: | fld f0,0(x1) | 1
 |  | fadd.d f4,f0,f2 | 2,3
 |  | fsd f4,0(x1) | 4,5,6
 |  | fld f6,8(x1) | 7
 |  | fadd.d f8,f6,f2 | 8,9
 |  | fsd f8,8(x1) | 10,11,12
 |  | fld f0,16(x1) | 13
 |  | fadd.d f12,f0,f2 | 14,15
 |  | fsd f12,16(x1) | 16,17,18
 |  | fld f14,24(x1) | 19
 |  | fadd.d f16,f14,f2 | 20,21
 |  | fsd f16,24(x1) | 22,23,24
 |  | addi x1,x1,32 | 25
 |  | bne x1,x2,Loop | 26,27
 |  | Stall | 28
Notes: 指令调度

## Slide 56: Cost of The Code
This loop will run in 28 clock cycles
  14 instruction issue cycles
  14 stalls
7 clock cycles per iteration
8 Registers
  Use different registers for each iteration

## Slide 57: Scheduling to Eliminate All Stalls
1 | Loop: | fld | f0,0(x1)
2 |  | fld | f6,8(x1)
3 |  | fld | f0,16(x1)
4 |  | fld | f14,24(x1)
5 |  | fadd.d | f4,f0,f2
6 |  | fadd.d | f8,f6,f2
7 |  | fadd.d | f12,f0,f2
8 |  | fadd.d | f16,f14,f2
9 |  | fsd | f4,0(x1)
10 |  | fsd | f8,8(x1)
11 |  | addi | x1,x1,32
12 |  | fsd | f12,-16(x1)
13 |  | bne | x1,x2,Loop
14 |  | fsd | f16,-8(x1)

## Slide 58: After Scheduling
The execution time of the unrolled loop has dropped to 14 clock cycles
  3.5 cycles per element of the four
Compared with
  Unrolled but not scheduling: 7 cycles per element
  Scheduled but not unrolled: 6 cycles per element

## Slide 59: Summary of Loop Unrolling
The key is to know
  WHEN and HOW the ordering among instructions may be changed
In practice, this process must be performed in a methodical fashion by
  A compiler or (and)
  Hardware

## Slide 60: Homework
Textbook: 3.1-3.2
Exercise
  Coding: write a piece code that unrolling our examples

## Slide 61: Next…
Dynamic Algorithms